## Slide 1: Legal Disclaimer
INFORMATION IN THIS DOCUMENT IS PROVIDED IN CONNECTION WITH INTEL® PRODUCTS. NO LICENSE, EXPRESS OR IMPLIED, BY ESTOPPEL OR OTHERWISE, TO ANY INTELLECTUAL PROPERTY RIGHTS IS GRANTED BY THIS DOCUMENT. EXCEPT AS PROVIDED IN INTEL'S TERMS AND CONDITIONS OF SALE FOR SUCH PRODUCTS, INTEL ASSUMES NO LIABILITY WHATSOEVER, AND INTEL DISCLAIMS ANY EXPRESS OR IMPLIED WARRANTY, RELATING TO SALE AND/OR USE OF INTEL PRODUCTS INCLUDING LIABILITY OR WARRANTIES RELATING TO FITNESS FOR A PARTICULAR PURPOSE, MERCHANTABILITY, OR INFRINGEMENT OF ANY PATENT, COPYRIGHT OR OTHER INTELLECTUAL PROPERTY RIGHT.
UNLESS OTHERWISE AGREED IN WRITING BY INTEL, THE INTEL PRODUCTS ARE NOT DESIGNED NOR INTENDED FOR ANY APPLICATION IN WHICH THE FAILURE OF THE INTEL PRODUCT COULD CREATE A SITUATION WHERE PERSONAL INJURY OR DEATH MAY OCCUR.
Intel may make changes to specifications and product descriptions at any time, without notice. Designers must not rely on the absence or characteristics of any features or instructions marked "reserved" or "undefined." Intel reserves these for future definition and shall have no responsibility whatsoever for conflicts or incompatibilities arising from future changes to them. The information here is subject to change without notice. Do not finalize a design with this information.
The products described in this document may contain design defects or errors known as errata which may cause the product to deviate from published specifications. Current characterized errata are available on request.
Contact your local Intel sales office or your distributor to obtain the latest specifications and before placing your product order.
This document contains information on products in the design phase of development.
All products, platforms, dates, and figures specified are preliminary based on current expectations, and are subject to change without notice. All dates specified are target dates, are provided for planning purposes only and are subject to change.
This document contains information on products in the design phase of development. Do not finalize a design with this information. Revised information will be published when the product is available. Verify with your local sales office that you have the latest datasheet before finalizing a design.
Intel processor numbers are not a measure of performance. Processor numbers differentiate features within each processor family, not across different processor families. See www.intel.com/products/processor_number for details.
Intel and the Intel logo are trademarks of Intel Corporation in the U.S. and other countries.
*Other names and brands may be claimed as the property of others.
Copyright © 2009, Intel Corporation. All rights reserved.

## Slide 2: Bit Manipulation
Netanel Kaufman and Niv Noach, Intel Corporation
Hebrew University, Jerusalem

## Slide 3: Introduction
Common programming involves manipulating basic data types (bytes, integers, doubles) and complex data types (structures, classes, arrays)
Smallest data type usually is 1 octet (i.e. ‘byte’ = 8 bits)
Working with low-level memory structures requires bit-level resolution
  Devices registers, network protocols, space-optimized data structures

## Slide 4: Example
An output device with 8 leds, controlled by writing 0/1 values to a special address in memory
Option 1:
  Writing 1 to address x set the 1st led, to address x+1 set the 2nd…
Option 2:
  All leds are controlled by writing a byte value to a specific location in memory – each bit of that byte controls a different led

## Slide 5: Example
Decimal value | Hex value | Binary value | 
0 | 0x00 | 0000 0000 | 
1 | 0x01 | 0000 0001 | 
2 | 0x02 | 0000 0010 | 
32 | 0x20 | 0010 0000 | 
170 | 0xAA | 1010 01010 | 
255 | 0xFF | 1111 1111 | 

## Slide 6: Controlling the Bits
There are several ways to control bits in a data type.
We will show example of the following, most common, two methods:
  Bit-wise operations
  Bit fields and unions

## Slide 7: Method #1 Bitwise Operations

## Slide 8: Bitwise Operations
Just like the ‘+’ operator sums two integers, there are operators in C for working on bits in another data type
Notice! Bitwise operators work on the entire data type, bit-by-bit

## Slide 9: Bitwise Operators in C
& - bitwise AND
| - bitwise OR
~ - bitwise NOT
^ - bitwise XOR
<< - left shift
>> - right shift

## Slide 10: Testing bits AND
#define DEVICE_REGISTER_ADDR 0x00010000
#define TEST_BIT_0 0x01
char *ptr = (char *) DEVICE_REGISTER_ADDR;
if (*ptr & TEST_BIT_0) {
/* Do something... /*
}
1111 0000 0xF0
& 0010 0010 & 0x22
0010 0000 0x20

## Slide 11: Setting bits OR
#define DEVICE_REGISTER_ADDR 0x00010000
#define SET_BIT_0 0x01
#define SET_BIT_1 0x02
#define SET_BIT_2 0x04
char *ptr = (char *) DEVICE_REGISTER_ADDR;
*ptr |= SET_BIT_0;
*ptr = SET_BIT_1 | SET_BIT_2
1111 0000 0xF0
| 0010 0010 | 0x22
1111 0010 0xF2

## Slide 12: Clearing bits AND NOT
#define DEVICE_REGISTER_ADDR 0x00010000
#define CLEAR_BIT_3 0x08
char *ptr = (char *)(DEVICE_REGISTER_ADDR );
*ptr = *ptr &~CLEAR_BIT;
*ptr &= ~CLEAR_BIT;
1111 0000 0xF0
&~ 0010 0010 &~ 0x22
1101 0000 0xD0

## Slide 13: Toggling bits XOR
#define DEVICE_REGISTER_ADDR 0x00010000
#define TOGGLE_BIT_4 0x10
char *ptr = (char *) DEVICE_REGISTER_ADDR ;
*ptr ^= TOGGLE_BIT;
1111 0000 0xF0
^ 0010 0010 ^ 0x22
1101 0010 0xD2

## Slide 14: Shifting bits
1111 0000
>> 0000 0010
0011 1100
1111 0000
<< 0000 0001
1110 0000
#define BIT_0 ( 1 << 0 )
#define BIT_1 ( 1 << 1 )
#define BIT_2 ( 1 << 2 )
#define BIT_3 ( 1 << 3 )

## Slide 15: Shifting bits
// Efficiently divide and multiply by 2^k
unsigned int n = 1024;
unsigned int half = n >> 1; // half == 512
unsigned int twice = n << 1; // twice == 2048
unsigned char mask;
for (mask = 0x1; mask; mask <<= 1 ) {
if ( *ptr & mask ) {
/* Do somthing... /*
}
}

## Slide 16: Bit Manipulation Examples
void SetMultiBitField(int *reg, int val) {
/* Set bits 2-4 of reg to val */
val &= 0x7; // make sure val’s value is valid (0x0-0x7)
val <<= 2; // shift it to place
*reg &= ~(0x7<<2); // clear the old value
*reg |= val; // set the new value
// or equivalently, do all in one shot:
// *reg = (*reg &~ 0x1C) | ( (val & 0x7) << 2 );
}

## Slide 17: Bit Manipulation Examples
#if defined(BIG_ENDIAN)
#define htons(A) (A) #else
#define htons(A) ((((uint16)(A) & 0xff00) >> 8) | \ (((uint16)(A) & 0x00ff) << 8)) #endif
The htons() function converts the unsigned short integer from host byte order to network byte order.

## Slide 18: Method #2 Bit Fields (and unions)

## Slide 19: Bit fields
Compound data types which treat every bit (or groups of bits) in it separately

## Slide 20: Bit Fields - Sample
struct _bits
{
unsigned int bit0 : 1;
unsigned int bit1 : 1;
unsigned int bit2 : 1;
unsigned int bit3 : 1;
unsigned int nibble : 4;
} bits;
bits.bit0 = 0;
bits.bit1 = 1;
bits.bit2 = 0;
bits.bit3 = 1;
bits.nibble = 0xA;
/* bit# 7654 3210 */
/* == 1010 1010 */

## Slide 21: Union
typedef union
{
unsigned int a;
unsigned char b[4];
} U;
Some compiler requires use of union
A Union is like a structure, except that each element shares the same memory.
typedef struct
{
unsigned int a;
unsigned char b[4];
} S;
0x10001
0x10002
0x10003
0x10004
0x10005
0x10006
0x10007
0x10008
0x10008
0x10000
0x10001
0x10002
0x10003
0x10004
0x10005
0x10006
0x10007
0x10008
0x10008
0x10000
a
a
b[0]
b[1]
b[2]
b[3]
b[0]
b[1]
b[2]
b[3]

## Slide 22: Union
typedef union
{
unsigned char byte;
struct
{
unsigned char bit0 : 1;
unsigned char bit1 : 1;
unsigned char bit2 : 1;
unsigned char bit3 : 1;
unsigned char nibble : 4;
} bits;
} Bitfield;
Bitfield * bitfield = (Bitfield *)(0x00100000);
bitfield->byte = 0;
bitfield->bits.bit1 = 1; // bitfield->byte == 0x2
Some compiler requires use of union
Also provides a convenient access to the value

## Slide 23: Bit Fields
typedef union
{
unsigned int word;
struct
{
unsigned char bit0 : 1;
unsigned char : 1; // 1 bit unnamed placeholder
unsigned char bit2 : 1;
unsigned char bit3 : 1;
unsigned short :0; // pad to short boundary
unsigned char nibble1 : 4;
unsigned char :0; // pad to char boundary
unsigned char nibble2 : 4;
} bits;
} Bitfield;
Bitfield bf;
bf.word = 0;
bf.bits.bit0 = bf.bits.bit2 = bf.bits.bit3 = 1;
bf.bits.nibble1 = bf.bits.nibble2 = 0xF;
/* bf.word == 0xf0f000d */

## Slide 24: Bit Fields
Cons:
  Can be less efficient - each bit change is actually a read-modify-write
  Portability issues
Pros:
  Individual bit fields may be declared volatile or const
  Ease of use, code clarity